## Slide 1: On support of larger max TBS for TDD UL in eMTC
Huawei, HiSilicon, CATR, CMCC Xinwei
3GPP TSG RAN WG1 Meeting #84 R1-161266
St Julian’s, Malta, February 15th-19th, 2016
Agenda Item: 7.1.5

## Slide 2: Proposal
The max TBS size is approximately 3000 bits for TDD Uplink in eMTC
  Determined by reusing the legacy TBS table.
Decide in this meeting the max TBS size for TDD Uplink through the following:
  Option A: Max TBS=3240. The size of MCS field in DCI format 6-0A is 5 bits for TDD.
  Option B: Max TBS=3112. If NPRB=6, TBS is determined based on NPRB=10; otherwise, the same as legacy operation.

## Slide 3: Example: Option A
ITBS | NPRB |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
0 | 16 | 32 | 56 | 88 | 120 | 152
1 | 24 | 56 | 88 | 144 | 176 | 208
2 | 32 | 72 | 144 | 176 | 208 | 256
3 | 40 | 104 | 176 | 208 | 256 | 328
4 | 56 | 120 | 208 | 256 | 328 | 408
5 | 72 | 144 | 224 | 328 | 424 | 504
6 | 328 | 176 | 256 | 392 | 504 | 600
7 | 104 | 224 | 328 | 472 | 584 | 712
8 | 120 | 256 | 392 | 536 | 680 | 808
9 | 136 | 296 | 456 | 616 | 776 | 936
10 | 144 | 328 | 504 | 680 | 872 | 1032
11 | 176 | 376 | 584 | 776 | 1000 | 1192
12 | 208 | 440 | 680 | 904 | 1128 | 1352
13 | 224 | 488 | 744 | 1000 | 1256 | 1544
14 | 256 | 552 | 840 | 1128 | 1416 | 1736
15 | 280 | 600 | 904 | 1224 | 1544 | 1800
16 | 328 | 632 | 968 | 1288 | 1608 | 1928
17 | 336 | 696 | 1064 | 1416 | 1800 | 2152
18 | 376 | 776 | 1160 | 1544 | 1992 | 2344
19 | 408 | 840 | 1288 | 1736 | 2152 | 2600
20 | 440 | 904 | 1384 | 1864 | 2344 | 2792
21 | 488 | 1000 | 1480 | 1992 | 2472 | 2984
22 | 520 | 1064 | 1608 | 2152 | 2664 | 3240
-If the UE is not capable of supporting 64QAM in PUSCH or has been configured by higher layers to transmit only QPSK and 16QAM, is first read from Table 8.6.1-1. The modulation order is set to

## Slide 4: Example: Spec impact on 36.213 by Option A
-If the UE is not capable of supporting 64QAM in PUSCH or has been configured by higher layers to transmit only QPSK and 16QAM, is first read from Table 8.6.1-1. The modulation order is set to
MCS Index | Modulation Order | TBS Index
0 | 2 | 0
1 | 2 | 1
2 | 2 | 2
3 | 2 | 3
4 | 2 | 4
5 | 2 | 5
6 | 2 | 6
7 | 2 | 7
8 | 2 | 8
9 | 2 | 9
10 | 2 | 10
11 | 4 | 10
12 | 4 | 11
13 | 4 | 12
14 | 4 | 13
15 | 4 | 14
16 | 4 | 15
17 | 4 | 16
18 | 4 | 17
19 | 4 | 18
20 | 4 | 19
21 | 6 | 19
22 | 6 | 20
23 | 6 | 21
24 | 6 | 22

## Slide 5: Example: Spec impact on 36.306 by Option A
UE UL Category | Maximum number of UL-SCH transport block bits transmitted within a TTI | Maximum number of bits of an UL-SCH transport block transmitted within a TTI | Support for 64QAM in UL
UL Category 0 (Note 1) | 1000 | 1000 | No
UL Category 3 | 51024 | 51024 | No
UL Category 5 | 75376 | 75376 | Yes
UL Category 7 | 102048 | 51024 | No
UL Category 8 | 1497760 | 149776 | Yes
UL Category 13 | 150752 | 75376 | Yes
UL Category 14 | 9585664 | 149776 | Yes
NOTE 1: Within one TTI, a UE indicating category 0 and reduced bandwidth operation shall be able to transmit up to 3240 bits for a transport block associated with C-RNTI/Semi-Persistent Scheduling C-RNTI for TDD. |  |  | 
Table 4.1A-2: Uplink physical layer parameter values set by the field ue-CategoryUL

## Slide 6: Example: Option B
ITBS | NPRB |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 10
0 | 16 | 32 | 56 | 88 | 120 | 256
1 | 24 | 56 | 88 | 144 | 176 | 344
2 | 32 | 72 | 144 | 176 | 208 | 424
3 | 40 | 104 | 176 | 208 | 256 | 568
4 | 56 | 120 | 208 | 256 | 328 | 696
5 | 72 | 144 | 224 | 328 | 424 | 872
6 | 328 | 176 | 256 | 392 | 504 | 1032
7 | 104 | 224 | 328 | 472 | 584 | 1224
8 | 120 | 256 | 392 | 536 | 680 | 1384
9 | 136 | 296 | 456 | 616 | 776 | 1544
10 | 144 | 328 | 504 | 680 | 872 | 1736
11 | 176 | 376 | 584 | 776 | 1000 | 2024
12 | 208 | 440 | 680 | 904 | 1128 | 2280
13 | 224 | 488 | 744 | 1000 | 1256 | 2536
14 | 256 | 552 | 840 | 1128 | 1416 | 2856
15 | 280 | 600 | 904 | 1224 | 1544 | 3112