## Slide 1: WF on the UE-SS Starting Subframe for eMTC
???
R1-161378
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th – 19th February 2016
Agenda item 7.1.5

## Slide 2: Proposal Choices
Initial Starting Subframe
  Option A: Fixed Start SF for all UE-SS, SF=0 for SFN=0
    Always SFN=0, SF=0
  Option B: Offset Start SF based on randomised rule
    Option B1: Cell Specific: Mod (PCID, StartSF_Periodicity}
    Option B2: UE Specific: Mod (C-RNTI, StartSF_Periodicity}
  Option C: Offset Start SF based on explicit configuration upto SF=10239
    mpdcch-StartSF-UESS-r13 increased from {0,1,...,7} to {0,1,2,..., 10239}
Start Subframe Periodicity
  Indexed by RRC mpdcch-StartSF-UESS-r13 or new RRC parameter
    Option 2: Rmax*G, G= {1, 2, 3, 4, 5, 6, 7, 8}
    Option 3: Rmax*G, G= {1, 2, 4, 5, 8, 10, 16, 20}
Handling of SFN wrap-around
  If SFN wrap-around is an issue then:
    Option 1: Discard last Rmax if overlaps the next SFN

## Slide 3: Option 1 – Fixed common start SF
For MPDCCH UE-specific search space, and Type0-MPDCCH common search space, is given by ,
where
  T=Rmax*G, G {1, 2, 4, 5, 8, 10, 16, 20} and the index of one element is given by the higher layer parameter mPDCCH-startSF-UESS.

## Slide 4: Option 2 - Randomized Starting SF
For MPDCCH UE-specific search space, and Type0-MPDCCH common search space, is given by ,
where
  T=Rmax*G, G {1, 2, 3, 4, 5, 6, 7, 8} and the index of one element is given by the higher layer parameter mPDCCH-startSF-UESS.
  δ = Choose between the following alternatives:
    Option 2A: PCID mod ( T )
    Option 2B: C-RNTI mod (T)

## Slide 5: Option 3 – Explicitly signaled starting SF
For MPDCCH UE-specific search space, and Type0-MPDCCH common search space, is given by ,
where
  T=Rmax*G, G {1, 2, 3, 4, 5, 6, 7, 8} and the index of one element is given by NEW higher layer parameter mPDCCH-periodicity-coeff.
  δ = Modified Higher parameter mPDCCH-startSF-UESS
    Modification is a RANGE extension from 0...7 to 0...10239