## Slide 1: WF on LAA UL LBT Mechanisms
Broadcom, CableLabs, BlackBerry, Orange,..
3GPP TSG RAN WG1 #84 R1-161382
St. Julian, Malta
15th –19th February 2016
Agenda item: 7.3.1.5
Document for decision

## Slide 2: Background
Design of Uplink Channel access is a part of Release 14 eLAA where the following aspects must be finalized and which are also of significance to coexistence with other technologies in the unlicensed spectrum
  The type of LBT followed before a UL transmission or UL grant (No-UL-LBT, Single-shot fixed LBT, Cat4 LBT)
  The parameters used for LBT if performed
  The dependence of the LBT algorithm and parameters on whether self-carrier or cross-carrier scheduling is used.
  The Energy detection threshold used before a UL transmission whenever LBT is used

## Slide 3: Proposal 1
If the UL grant in case of self-carrier scheduling is transmitted standalone,
  It shall use the same channel access priority and LBT parameters as the DL PDSCH corresponding to the UL data.

## Slide 4: Proposal 2
If the UL grant in case of self-carrier scheduling is transmitted together with other PDSCH data:
  Lower priority PDSCH transmissions shall not be piggybacked with the transmission of the UL grant in case the channel access has been obtained using the access priority of the UL grant.
  If the UL grant is piggybacked with PDSCH transmissions of the same access priority class as the UL grant, then the corresponding UL transmission can use the Fixed UL LBT schemes.
  If the UL grant is piggybacked with higher priority PDSCH transmissions where the channel access has been obtained using the access priority of the higher priority PDSCH, then the corresponding UL transmission shall not use the Fixed UL LBT scheme

## Slide 5: Proposal 3
If the UL transmission corresponding to the UL grant occurs in a different TXOP, the UL transmission must not use Fixed UL LBT irrespective of the LBT performed before the UL grant.

## Slide 6: Proposal 4
If a one shot fixed LBT is used for LAA UL, it shall consider the following:
  Include an idle CCA slot at the start.
  Define the timing and duration of channel sensing within the LBT duration
  Evaluate whether a fixed LBT duration of 25us is sufficient to ensure fair coexistence with co-channel Wi-Fi.

## Slide 7: Proposal 5
For cases when relaxed UL LBT is considered,
  No-UL-LBT shall not be an option
  LAA shall use fixed LBT for Uplink transmissions instead of no-UL-LBT

## Slide 8: Proposal 6
For cross-carrier scheduled UL grant, when LBT is not performed on the SCell on which the UL transmission would be performed,
  UL LBT shall be like DL LBT and the LBT parameters shall be similar to the LBT parameters used by Wi-Fi STA (as recommended by WFA) for the priority class of the UL data

## Slide 9: Proposal 6
The ED threshold used for UL LBT shall be -72 dBm or lower and shall not depend on the instantaneous transmit power of the UE