## Slide 1: WF on NB-IoT Timing Relationships
Huawei, HiSilicon, Neul, Intel, QC, u-blox…
R1-161389
3GPP TSG RAN WG1 Meeting #84
St. Julian’s, Malta, 15th - 19th February 2016
Agenda item 7.2.1.3

## Slide 2: Background
NB-IoT is targeting “ultra-low cost” UEs
The latency requirements for NB-IoT are considerably relaxed compared with LTE, due to the different nature of the target applications
The timing relationships used in LTE can impose very high peak processing load and complexity on the UE, but are unnecessary given the relaxed latency requirements for NB-IoT compared with LTE
Therefore, the timing relationships for NB-IoT can be relaxed compared with LTE
  For example NB-PDCCH -> NB-PUSCH and NB-PDSCH -> UL A/N

## Slide 3: Proposals
The start of UL A/N transmission is at least 12 milliseconds later than the end of the corresponding NB-PDSCH transmission
UE is not required to monitor more than:
  3 NB-PDCCH blind decoding candidates in any subframe when the candidates include repetition level 1
  4 NB-PDCCH blind decoding candidates in any subframe when the candidates do not include repetition level 1
The start of NB-PUSCH transmission is at least 8 milliseconds later than the end of its associated NB-PDCCH search space