## Slide 1: WF on Paging MPDCCH for eMTC
Ericsson, Nokia, ALU, ASB, NEC, LGE, InterDigital
R1-161403
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th – 19th February 2016
Agenda item 7.1.5

## Slide 2: Background (1)
RAN1#83 agreement:
  How to indicate set of M-PDCCH narrowband(s) for paging
    implicit mapping
      1st narrowband = PCID mod N_NB_paging
      Other narrowbands are in consecutive order from 1st narrowband with wrap-around
  When more than one narrowband is configured for M-PDCCH for paging
    The narrowband is up to RAN2

## Slide 3: Background (2)
RAN1#83 agreement: Frequency hopping for SIB1bis is given by –
  S is a set of valid DL narrowbands for SIB1bis, the narrowband is indexed in the order of increasing value
    S = {s0, s1, s2, …., sK-1}, K = number of valid DL narrowbands for SIB1bis
  For system BW less than 12 RBs
    SIB1bis is transmitted in narrowband sj where j = PCID mod K
  For system BW between 12-50 RBs
    1st NB is sj where j = PCID mod K; 2nd NB is (sj + floor(K/2)) mod K
    Starting at SFN mod 8 = 0, SIB1bis transmission cycles through {1st NB, 2nd NB}
  For system BW between 51-110 RBs
    1st NB is sj where j = PCID mod K; 2nd NB is (sj + floor(K/4)) mod K
    3rd NB is (sj + 2*floor(K/4)) mod K; 4th NB is (sj + 3*floor(K/4)) mod K
    Starting at SFN mod 8 = 0, SIB1bis transmission cycles through {1st NB, 2nd NB, 3rd NB, 4th NB}
For BW > 3 MHz, the two middle narrowbands are not used for SIB1bis transmission

## Slide 4: Background (3)
RAN1#83 agreement:
  Frequency hopping pattern for M-PDCCH, PDSCH, PRACH, PUSCH, PUCCH is given by a fixed pattern
    For 2 narrowbands: cycle through {1st NB, 2nd NB}
    For 4 narrowbands (only applicable to M-PDCCH/PDSCH): cycle through {1st NB, 2nd NB, 3rd NB, 4th NB}
  Frequency hopping configuration for M-PDCCH: the first narrowband is signaled, the other narrowband(s) are determined using a single configurable offset (cell-specific)

## Slide 5: Proposal 1
For BW > 3 MHz, the two middle narrowbands are not used for Paging transmission
  Reuse set S:
    S = {s0, s1, s2, …., sK-1}, K = number of valid DL narrowbands for SIB1bis and paging MPDCCH
  Implicit paging MPDCCH narrowband definition
    1st NB is sj where j = PCID mod K;
    Other narrowbands are in consecutive order from 1st narrowband with wrap-around
    (sj, sj+1, …,sj+m…,sj+N_NB_paging-1)
    Wrap around means (sj+m => smod(j+m,N_NB_paging) )

## Slide 6: Proposal 2
When frequency hopping is enabled for paging MPDCCH, frequency hopping narrowbands other than the first narrowband are determined the same way as other MPDCCH, i.e.,
  First narrowband index for the FH pattern is
    n=0: first narrowband in the FH pattern is sj
    n=1: first narrowband in the FH pattern is sj+1, …
    n=N_NB_paging-1: first narrowband in the FH pattern is sj+N_NB_paging-1
  where n is derived from PO/PF calculation and (sj, sj+1, …,sj+m…,sj+N_NB_paging-1) are the valid DL narrowbands
  The other narrowband(s) in the FH pattern are determined using mpdcch-pdsch-HoppingOffset (cell-specific RRC parameter defined for MPDCCH/PDSCH in general)