## Slide 1: WF on PRACH starting subframe for eMTC
Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Nokia Networks, Panasonic
R1-161404
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th – 19th February 2016
Agenda item 7.1.5

## Slide 2: Proposal
Range for the RRC parameter for PRACH starting subframe periodicity:
  prachStartingSubframe = {2, 4, 8, 16, 32, 64, 128, 256}
  expressed in terms of PRACH opportunities
Offset (to allow TDM between different PRACH CE levels):
  N*prachStartingSubframe + numRepetitionPerPreambleAttempt
  expressed in terms of PRACH opportunities
  N = {0, …}
Note: according to the current CRs,
      numRepetitionPerPreambleAttempt = {1, 2, 4, 8, 16, 32, 64, 128}
      No starting subframe with absolute subframe number > 10240 - numRepetitionPerPreambleAttempt is allowed

## Slide 3: Example
PRACH CE level 0:
  numRepetitionPerPreambleAttempt = 1
  prachStartingSubframe = 8
   offset = N*8 + 1 = {1, 9, …}
PRACH CE level 1:
  numRepetitionPerPreambleAttempt = 2
  prachStartingSubframe = 8
   offset = N*8 + 2 = {2, 10, …}
PRACH CE level 2:
  numRepetitionPerPreambleAttempt = 4
  prachStartingSubframe = 8
   offset = N*8 + 4 = {4, 12, …}
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15