## Slide 1: Way forward on CA feature groups
Huawei, HiSilicon, CMCC, CATT, CATR, ZTE, Lenovo, Softbank, Nokia
3GPP TSG RAN WG1 #84 R1-161414 Julian’s, Malta, 15th - 19th February 2016
Agenda item: 7.1.6

## Slide 2
  Two feature groups for HARQ codebook size determination
      Fixed codebook size operation
        Mandatory for UEs supporting DL CA
      DAI based codebook size adaptation
        Mandatory for UEs supporting DL CA with more than 5 CCs
        For UEs supporting DL CA with no more than 5CCs
          Mandatory for UEs supporting TDD-TDD CA and TDD-FDD CA with TDD Pcell and more than 22bit HARQ-ACK
          Optional or not applicable for UEs supporting FDD-FDD CA and TDD-FDD CA with FDD Pcell with no more than 5 CCs
(Note: agreement in RAN1#82bis:
  Both solution (a) and solution (b) are mandatory feature as UE capability from RAN1 recommendation point of views for UEs supporting more than 5 CCs)

## Slide 3
Single UE feature group for the support of PUCCH format 4
  Mandatory for UEs supporting DL CA with more than 5 CCs
  Mandatory for UEs supporting TDD-TDD CA and TDD-FDD CA with TDD Pcell with no more than 5 CCs
  Optional or not applicable for UEs supporting FDD-FDD CA and TDD-FDD CA with FDD Pcell with no more than 5 CCs
Single UE feature group for the support of PUCCH format 5
  Optional for UEs supporting DL CA with more than 5 CCs
  Not applicable for UEs supporting DL CA with no more than 5CCs