## Slide 1: Way forward on simulation results and methodology
Ericsson, …
R1-161422
Ag 7.3.4.2
RAN1 #84 Malta
February 15-19 2016

## Slide 2: Background
Despite the agreed assumptions in R1-157806, different trends in the results of different companies are observed and may be due to remaining mismatch in the simulation assumptions
Moreover, it is beneficial to use a common format for reporting results

## Slide 3: Proposal for system-level simulations
The results are reported according to the format shown in the next slide
  Information about simulation end time and how the TCP connection is maintained is reported, e.g. in the notes field of the table

## Slide 4: Format to report system-level results
Reported parameters |  | Low load RU range for legacy TTI: 10%~25% |  |  |  |  | Medium load RU range for legacy TTI: 35%~50% |  |  |  |  | High load RU range for legacy TTI: above 55% |  |  |  | 
 |  | 14 OS | 7OS | 3/4OS | 2OS | 1OS | 14 OS | 7OS | 3/4OS | 2OS | 1OS | 14 OS | 7OS | 3/4 OS | 2OS | 1OS
DL: UPT CDF [Mbps] | 5% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 50% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 95% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Mean |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
DL: Delay CDF [s] | 5% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 50% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 95% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Mean |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RU |  | 0.2 |  |  |  |  | 0.4 |  |  |  |  | 0.6 |  |  |  | 
𝜆 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Notes: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
𝜆 is the arrival intensity of the Poisson process for generating files
RU is the resource utilization.
This table compares the 5th, 50th, 95th and average user perceived throughput (UPT) and the 5th, 50th, 95th and average delay for different system loads. Here the loads correspond to 20%, 40%, 60% RU for the reference case (=legacy TTI).

## Slide 5: Proposal for sPUSCH and sPDSCH link level results
The same number of PRBs for sPUSCH/sPDSCH is assumed when comparing different sTTI lengths
  Simulations assuming different numbers of PRBs for different sTTI lengths are optional
RB bundling for DMRS based channel estimation is studied
  Companies provide the number of bundled PRBs
CRS based channel estimation can use long-term channel filtering on CRSs before the end of the sTTI
The reported metrics include the SINR at 10% BLER and the throughput at 10% BLER
sTTI length | 1 symbol | 2 symbols | 3 symbols | 4 symbols | 7 symbols | 14 symbols
QPSK 1/3 |  |  |  |  |  | 
16QAM 3/4 |  |  |  |  |  | 
64QAM 5/6 |  |  |  |  |  | 

## Slide 6: Proposal for s(E)PDCCH link level results
CRS based channel estimation can use long-term channel filtering on CRSs before the end of the sTTI
The reported metric includes the SINR at 1% BLER
 | 1 CCE | 2 CCEs | 4 CCEs | 8 CCEs
40 bits |  |  |  | 
70 bits |  |  |  | 

## Slide 7: Proposal for PUCCH link level results
The reported metric is the smallest SNR at which all three following conditions are valid
  ACK missed detection probability <= 1%
  NACK-to-ACK error probability <= 0.1%
  DTX-to-ACK probability <= 1%
sTTI length | 2 symbols | 3 symbols | 4 symbols | 7 symbols | 14 symbols