## Slide 1: WF on hopping patterns of NB-PRACH
Huawei, HiSilicon, Ericsson
R1-161428
3GPP TSG RAN WG1 Meeting #84
St. Julian’s, Malta, 15th - 19th February 2016
Agenda item 7.2.1.2.2

## Slide 2: Background
Agreements:
NB-PRACH uses a subcarrier spacing of 3.75kHz
2 CP lengths are provided to support different cell sizes
  66.7 us and 266.7 us
Hopping is between groups of 6 symbols
  Details of hopping pattern FFS
First level fixed size hopping is used between 1st/2nd and between 3rd/4th symbol groups
Second level hopping is used between 2nd/3rd symbol groups:
  Details of 2nd level hopping FFS till Friday (e.g. based on LTE PUSCH type 2 hopping or fixed hopping)

## Slide 3: Benefits of pseudo random hopping
Avoid false alarm response in overlapping cells overhearing NB-PRACH from neighboring cells
Reduce inter-cell and intra-cell interference
Allow flexible configuration

## Slide 4: Proposal
The size of of 2nd level hopping between 2nd/3rd symbol groups is fixed to 6 tones
Pseudo random hopping is supported across the repetitions of basic unit (4 groups) .
  The random hopping pattern is LTE PUSCH type 2 hopping
    The total size of the random hopping is within 12 tones.

## Slide 5: Example hopping pattern