## Slide 1: WF on NB-PDCCH search space
Huawei, HiSilicon, …
R1-161430
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th – 19th February 2016
Agenda item 7.2.1.1.2

## Slide 2: Background
Agreement:
CSS is defined for RAR (as well as paging)
UE is not required to simultaneously monitor NB-PDCCH USS and CSS
Max aggregation level for NB-PDCCH: 2
  Repetition is only applied in case AL=2
For USS, UE only searches in its configured set of ALs and numbers of repetitions of PDCCH

## Slide 3: Proposals
UE monitors one of the following sets of {AL, #repetition, #blind decodes}:
  {1, 1, 2}, {2, Rmax/2, 1}, {2, Rmax, 1} when Rmax ≤
  {2, Rmax/4, 1}, {2, Rmax/2, 1}, {2, Rmax, 1} when ≤ Rmax ≤
  {2, Rmax/8, 1}, {2, Rmax/4, 1}, {2, Rmax/2, 1}, {2, Rmax, 1} when ≤ Rmax ≤
  Rmax is the configured maximum number of repetitions of NB-PDCCH
  < < - decide these values in CR phase
The same configuration options apply to CSS and USS
The configuration can be different between CSS and USS