## Slide 1: WF on NB-PDCCH Multiplexing
Intel Corporation
3GPP TSG RAN WG1 Meeting #84 R1-161435
St Julian’s, Malta, 15th - 19th February 2016

## Slide 2: Background
A CCE for NB-PDCCH is composed by resources within a subframe
  within a PRB pair, 2 CCEs are defined
  NB-PDCCH and NB-PDSCH are multiplexed only based on TDM at subframe level at least per UE
  Different NB-PDCCHs:
  TDM at subframe level for extended and extreme coverage.
  Can be multiplexed in one subframe for normal coverage
  FFS: FDM+TDM
Mapping of 2 CCEs: Upper 6 subcarriers are allocated to one CCE and lower 6 subcarriers are allocated to the other CCE within a PRB pair.
Max aggregation level for NB-PDCCH: 2
  Repetition is only applied in case AL=2

## Slide 3: Proposal for NB-PDCCH Multiplexing
For aggregation level two, the two CCEs of one NB-PDCCH are mapped to the same subframe