## Slide 1: WF on NB-PDSCH Scrambling
Intel Corporation, MediaTek, ZTE
3GPP TSG RAN WG1 Meeting #84 R1-161436
St Julian’s, Malta, 15th - 19th February 2016

## Slide 2: NB-PDSCH Scrambling
The scrambling sequence for NB-PDSCH is according to Section 7.2 of TS 36.211
If the codeword is mapped to more than one subframe, the scrambling sequence generator is initialised at the start of each codeword and at the start of each repetition thereof, i.e., after each potential “early termination point”
If the codeword is mapped to a single subframe, the scrambling sequence initialization is FFS
The initialisation value cinit is according to Section 6.3.1 of TS 36.211 for the LTE PDSCH
  FFS: cinit also depends on the radio frame number and/or repetition number in case scheduling window is agreed
Note: support of symbol level combining is not precluded (see Appendix)

## Slide 3: Appendix: Examples of possible RE mappings
TTI
TTI
TTI
early termination point
early termination point
early termination point
frequency tracking error precludes symbol combining of similar subframes
TTI
first early termination point
symbol combining possible between adjacent subframes since frequency tracking is relatively stable between subframes
TTI
first early termination point
symbol combining possible between adjacent subframes since frequency tracking is relatively stable between subframes
repetition cycle
TTI