## Slide 1: WF on TPSK for UL single-tone transmissions
Qualcomm, Samsung, Huawei, HiSilicon, Neul, Vodafone, CMCC, CATR, KDDI, China Unicom, China Telecom, Potevio, IITH,CEWiT, Reliance-Jio
R1-161470
3GPP TSG RAN WG1 #84
St Julian’s, Malta, 15th – 19th February 2016
Agenda item 7.2.1.2.1

## Slide 2: Background
In the WID [RP-152284], it has specified that
  For the uplink:
    Single tone transmissions are supported. Two numerologies should be configurable by the network for single-tone transmission: 3.75 kHz and 15 kHz. A cyclic prefix is inserted. Frequency domain sinc pulse-shaping in the physical layer description.
    Multi-tone transmissions are supported, based on SC-FDMA with 15 kHz UL subcarrier spacing.
    FFS: Additional mechanisms for PAPR reduction.
    The UE shall indicate the support single-tone and/or multi-tone, details to be discussed by RAN WGs
  For single-tone transmissions, TPSK modulation can achieve higher peak data rate and maintain the same PAPR as single-tone modulation with BPSK and QPSK.

## Slide 3: Proposal
For a UE that indicates the support of only single-tone transmissions, the following TPSK modulation formats are supported in the UL
  (2,4)-TPSK and (4,4)-TPSK with contiguous tone allocation as specified in Tables 2 and 3, respectively, in R1-160881.
  Other related specifications are discussed in the following slides-.

## Slide 4: Related Specifications-DCI
Subcarrier indication in DCI
  A total of 48 possible tone location for single-tone transmission without TPSK: 6 bits needed.
  For 3.75 kHz tone spacing
    16 subcarrier allocations for TPSK, 12 for (2,4)-TPSK starting at tone 12, 14, …34, and 4 for (4,4,) –TPSK starting at tone 16, 20, 24, 28.
  For 15 kHz tone spacing
    There are a total 30 single and multi-tone subcarrier allocations excluding TPSK: 12 for single tone, 10 for 3-tone, 7 for 6-tone, and 1 for 12-tone allocations.
    Add 11 for 2-tone allocations (2,4)-TPSK, 9 for 4-tone allocations (4,4)-TPSK.
MCS/TBS size
  3bits: 8 MCS for single-tone, 8 MCS for multi-tone, 4 or 6 for TPSK.

## Slide 5: Related Specifications-Reference Signal
A reference signal pattern is defined by two sequences:
  A tone sequence that defines the tone to be used at each pilot symbol.
    Two tone sequence for (2,4)-TPSK as [0 1 0 1 0 1 0 1 0 1 01] and [1 0 1 0 1 0 1 0 1 0 1 0]
    Four tone sequences for the (4,4)-TPSK as [0 1 3 0 1 3], [3 2 0 3 2 0], [1 0 3 1 0 3],[2 3 0 2 3 0].
  A signal sequence that determines the signal to be transmitted at each pilot symbol.
    Same design as the single-tone transmission reference signal without rotation.