## Slide 1: NB-IoT Synchronization Signal Design
3GPP TSG RAN WG1 #84 R1-161485
St. Julian’s, Malta, 15th – 19th February 2016
Agenda item: 7.2.1.1.4
LG Electronics

## Slide 2: Proposal on NB-IoT PSS
  Root indices = [5 6 5 6 5 6 5 6 5 6 5]
  Sign over 11 OFDM symbols = [1 1 -1 -1 1 -1 -1 1 -1 1 1]
    i.e., transmit 11 symbols corresponding to root index/sign of [5 6 -5 -6 5 -6 -5 6 -5 6 5]

## Slide 3
Appendix

## Slide 4: NB-PSS sequence proposal
Short ZC sequences with cover code
  Short ZC sequences are mapped to each OFDM symbol
    Number of ZC sequences: 2 (e.g., root index of 5 and 6)
    A pair of ZC sequences may have complex conjugate relation
    Sequence length: 11 (fit in OFDM symbol with cyclic extension)
  Binary cover code:
    Find cover code to have good correlation property: e.g.,) ={1, 1, -1, -1, 1, -1, -1, 1, -1, 1, 1}
  Sequence mapping to OFDM symbol: e.g.,) {z1, z2, z1, z2, z1, z2, z1, z2, z1, z2, z1}

## Slide 5: NB-PSS detection details
Detection flow of NB-PSS (single shot)
  Differential operation between adjacent received OFDM symbols
    Constant phase caused by CFO in each sample
    Assume 1.92 MHz sampling rate in the receiver
    : received NB-PSS signal
  Cross correlation between and modified reference NB-PSS signal
    Where is pre-generated by differential operation between adjacent OFDM symbols
    NB-PSS signal
  Obtain estimated timing by finding peak of correlator outputs
  CFO estimation with the obtained timing
If NB-PSS detection in a single subframe is not successful, perform detection over accumulated NB-PSS signals over multiple subframes
  Threshold test for the NB-PSS correlator output to have false alarm rate of 0.1 %

## Slide 6: NB-PSS detection details
Correlation property of depending on a cover code
With cover code (root index : 1) Without cover code (root index : 1)
With cover code (root indices : 5, 6) Without cover code (root indices : 5, 6)

## Slide 7: NB-PSS detection details
With cover code (root indices : 4, 5, 6, 7) Without cover code (root indices : 4, 5, 6, 7)
With cover code (root indices : 1, 2, 3, 4, 5, 6, 7, 8, 9, 10) Without cover code (root indices : 1, 2, 3, 4, 5, 6, 7, 8, 9, 10)

## Slide 8: NB-PSS detection details
  The cover code is essential to improve the correlation property.
  Without cover code, NB-PSS with 1, 2, or 4 ZC sequences shows bad correlation property
  In case of NB-PSS with 10 ZC sequences, cover code can improve correlation property
  There is no significant difference in correlation property (in terms of the 2nd peak performance) when the number of ZC sequences in NB-PSS is 2, 4, and 10 with cover code

## Slide 9: NB-PSS detection details
After differential operation, hierarchical correlation with binary cover code can be still applied to reduce computational complexity
  Computational complexity depends on the number of reference ZC sequences after differential operation
  Notation: N (short ZC sequence length), L(PSS burst length)
  Assume NB-PSS with 1 ZC sequence: e.g.,): same root index in each OFDM symbol
    The number of reference P(n) sequence is 1
    Computational complexity: N*L operation
  Assume NB-PSS with 2 ZC sequences: e.g.,): root index in each OFDM symbol {5,6,5,6,5,6,5,6,5,6,5}
    The number of reference P(n) sequence is 2: two sequences have complex conjugate relation
    Computational complexity: 2*N*L operation
    With complex conjugate relation, further complexity reduction may be possible
  Assume NB-PSS with 4 ZC sequences: e.g.,): root index in each OFDM symbol {5,6,4,7,5,6,5,7,5,6,4}
    The number of reference P(n) sequence is 3
    Computational complexity: 3*N*L operation
  Assume NB-PSS with 10 ZC sequences: e.g.,) {1,10,2,9,3,8,4,7,5,6,5}
    The number of reference P(n) sequence is 10: a pair of sequences have complex conjugate relation
    Computational complexity: 10*N*L operation
  The required memory to store the reference NB-PSS sequence will also increase when the number of reference ZC sequences increases
Reasonable compromise will be 2 ZC sequences in NB-PSS

## Slide 10: Evaluation assumption
Follow agreed simulation assumptions
Parameter | Value
Carrier Frequency | 900 MHz
Channel Model | TU1
Subcarrier Spacing | 15 kHz
BS transmit power | In-band: 46 dBm
Power boosting | 6 dB for in-band scenario
Target MCL value | 164 dB
Antenna Configuration | 1 Tx, 1 Rx
Timing offset | Uniformly distributed in [-0.5 ms, 0.5 ms]
Frequency Offset | Randomly selected value from [-25 KHz, 25 KHz]
Detection threshold value | False alarm probability of 0.1 % when only AWGN exists
# of interfering nodes | 0, 2 (same transmit power as that of serving node is assumed)
ZC sequence length | 11 (fit in OFDM symbol with cyclic extension)
PSS/SSS detection | Allow accumulation of multiple PSS/SSS subframes

## Slide 11: NB-PSS sequence comparison
Acquisition time performance according to the number of ZC sequences
  # of interfering node is 0
  # of interfering node is 2
# of ZC sequences | Detection probability (%) | Acquisition time (ms)
1 (with CC) | 98.89 | 2380
2 (with CC) | 99.47 | 1608
4 (with CC) | 99.45 | 1572
10 (with CC) | 99.80 | 1560
10 (without CC) | 99.66 | 1718
# of ZC sequences | Detection probability (%) | Acquisition time (ms)
1 (with CC) | 83.58 | 300
2 (with CC) | 96.15 | 220
4 (with CC) | 96.11 | 210
10 (with CC) | 96.64 | 200
10 (without CC) | 95.72 | 230