## Slide 1: Way forward on assumptions for multiple access evaluation
Huawei, HiSilicon, […]
3GPP TSG RAN WG1 Meeting #84bis R1-163560
Busan, Korea, 11th – 15th April 2016
Agenda Item: 8.1.3

## Slide 2: Background
NR should be,
Applicable to different usage scenario families, including eMBB, mMTC, and URLLC
Multiple access (MA), as one fundamental component of NR, should
Contribute to improve KPIs for different usage scenario families.
This WF is for technical comparison in 3GPP. ITU evaluation will be discussed separately.
Appropriate evaluation should be defined to compare different MA proposals
Evaluation method
Evaluation scenarios
Evaluation metrics
Evaluation parameters

## Slide 3: Proposal (Evaluation method)
Link-level simulation (LLS) and system-level simulation (SLS) are used for multiple access evaluation.
  LLS* is used for feasibility investigation of new MA proposals, comparison of different proposals in typical scenarios and provide possible initial down-selection of proposals.
  SLS is used for further comparison of down-selected proposals, and further verification with traffic/scheduling/multi-cell interference dynamics, if needed.
  * LLS includes LLS with optional analytical model.

## Slide 4: Proposal (Evaluation method)
Analytical way for
  Device battery life (for mMTC).

## Slide 5: Proposal (Evaluation scenarios)
MA evaluation should consider all the three usage scenario families defined in TR38.913
  eMBB, mMTC, and URLLC
The following evaluation scenarios are to be used
  eMBB: dense urban, urban macro, rural, indoor
  mMTC: urban coverage for massive connection
  URLLC: FFS
  Other scenarios (e.g., eV2X) are not precluded.

## Slide 6: Proposal (Evaluation metrics for LLS)
For LLS, consider the following as evaluation metrics
  General
    BLER vs SNR reported for UL and DL calibration
    BS and UE receiver complexity reported
  UL:
    Sum throughput v.s. SNR at given BLER level under different overloading factor*.
    Link budget (MCL with specific data rate)
    Other metrics FFS (e.g., Maximum overloading factor v.s. SNR at given user throughput)
  DL:
    Sum rate region
    Optional: Sum normalized user throughput (normalized by throughput in orthogonal case); Sum throughput with minimum throughput constraint for some users
* See Appendix

## Slide 7: Proposal (Evaluation metrics for SLS)
For SLS, the following are used as evaluation metrics
  eMBB: TRP spectrum efficiency and 5th percentile user spectrum efficiency; user experienced data rate and area traffic capacity; signaling overhead
  mMTC: Connection density with “connection efficiency” reported; latency for infrequent small packets; signaling overhead
  URLLC: Reliability for a target latency

## Slide 8: Proposal (Evaluation priority for RAN1#85)
Preliminary LLS evaluation results are encouraged to be provided for RAN1#85

## Slide 9: Proposal (Evaluation parameters – LLS for UL)
Parameters | Values or assumptions
Carrier Frequency | 2 GHz
Waveform | OFDM /SC-FDMA
Numerology | Same as Release 13
System Bandwidth | 10 MHz
Total resource blocks | 4RB, 12RB, 48RB
BS antenna configuration | 2/4 Rx as baseline 8Rx optional
UE antenna configuration | 1Tx
Transmission mode | TM1 (refer to TS36.213)
Modulation and coding | QPSK-1/2, QPSK-3/4, 16QAM-1/2 or equivalent MCS; LTE Turbo
SNR distribution of Multiple UEs | Equal average SNR Other distribution FFS
Propagation channel & UE velocity | EPA, EVA, ETU 3km/h, 30km/h, 120km/h
Max number of HARQ transmission | 1
Overloading factor | 100%, 200%, 300%, or higher

## Slide 10: Proposal (Evaluation parameters – LLS for DL)
Parameters | Values or assumptions
Carrier Frequency | 2 GHz
Waveform | OFDM
Numerology | Same as Release 13
System Bandwidth | 10 MHz
Total resource blocks | 4RB, 12RB, 48RB
BS antenna configuration | 2/4 Tx as baseline 8Tx optional
UE antenna configuration | 2 Rx
Transmission mode | TM2 as starting point (refer to TS36.213)
Modulation and coding | QPSK-1/2, 16QAM-1/2, 64QAM-1/2, or equivalent MCS; LTE Turbo
SNR distribution of Multiple UEs | Fixed gap {0, 5, 10, 15, 20} dB between UEs
Power allocation between UEs | Dynamic
Propagation channel & UE velocity | EPA, EVA, ETU 3km/h, 30km/h, 120km/h
Max number of HARQ transmission | 1
Number of users superposed | 2, 3 or more

## Slide 11: Proposal (Evaluation parameters – SLS for eMBB)
Parameters | Values or assumptions
Deployment scenario | Dense urban
Carrier Frequency | Around 4GHz
Simulation bandwidth | 20MHz
Layout | Single layer: - Macro layer: Hex. Grid
ISD | 200m
BS antenna configuration | 2/4/8 Tx/Rx as starting point
UE antenna configuration | 1 Tx and 2 Rx as starting point
User distribution and UE speed | Uniform distribution, 20 users per TRP or more 80% indoor (3km/h), 20% outdoor (30km/h)
Service profile | For TRP spectrum efficiency: full buffer For user experienced data rate: non-full buffer
Channel model | 3D UMi
Dense Urban

## Slide 12: Proposal (Evaluation parameters – SLS for eMBB)
Rural
Parameters | Values or assumptions
Deployment scenario | Rural
Carrier Frequency | Around 700MHz
Aggregated system bandwidth | 20MHz
Layout | Single layer: - Hex. Grid
ISD | 1732m
BS antenna configuration | 2/4/8 Tx/Rx as starting point
UE antenna configuration | 1 Tx and 2 Rx as starting point
User distribution and UE speed | Uniform distribution, 20 users per TRP or more 50% outdoor vehicles (120km/h) and 50% indoor (3km/h)
Service profile | For TRP spectrum efficiency: full buffer For user experienced data rate: non-full buffer
Channel model | RMa

## Slide 13: Proposal (Evaluation parameters – SLS for mMTC)
Urban coverage for massive connections
Parameters | Values or assumptions
Deployment scenario | Urban coverage for massive connections
Carrier Frequency | 700MHz
Network deployment including ISD | Macro only, Hex. Grid, ISD = 1732m
Device deployment | Indoor, and outdoor in-car devices
Maximum mobility speed | 20% of users are outdoor in cars (100km/h) 80% of users are indoor (3km/h)
Service profile | Non-full buffer with small packets
BS antenna configuration | 2/4 Tx/Rx as starting point
UE antenna elements | 1 Tx and 2 Rx as starting point

## Slide 14: Appendix

## Slide 15: Appendix: Definition of overloading factor
Overloading factor
  For spreading case:
    overloading factor= num of data layers (users) / spreading length (number of REs)
  For non-spreading case:
    overloading factor= num of data layers (users) on each RE
Layer 1~4
Spreading on 2 REs
Example:
Overloading factor = 2

## Slide 16: Appendix: UL LLS metrics illustration

## Slide 17: Appendix: DL LLS metrics illustration

## Slide 18: Appendix: DL LLS metrics illustration
Sum normalized user throughput (normalized by throughput in orthogonal case)
in which i represents the index of the user that are multiplexed together, and represent the power allocation to user i and its best MCS under the power allocation, respectively.
Sum throughput with minimum throughput constraint for some users.