## Slide 1: Way Forward on SLSS for V2V PC5
3GPP TSG RAN WG1 Meeting #84b R1-163628
Busan, Korea, 11th - 15th April 2016
Agenda Item: 7.3.2.4
Huawei, HiSilicon, Samsung, Sharp, ITRI, CATR, LG Electronics, NTT DOCOMO, Potevio, ….

## Slide 2: Background
SLSS transmitted from out-coverage UE directly synchronized with GNSS or GNSS equivalent with sufficient reliability is differentiated from SLSS_net with in coverage indicator 1
At least reuse priority order SLSS_net with in coverage indicator 1, SLSS_net with in coverage indicator 0, SLSS_oon
  FFS: Definition of SLSS_net, SLSS_oon
Working assumption: Priority of SLSS transmitted from in-coverage UE directly synchronized with GNSS or GNSS equivalent with sufficient reliability is the same as that of SLSS_net with in coverage indicator 1
  FFS: SLSS transmitted from in-coverage UE using GNSS or GNSS equivalent is configured by eNB
    FFS: whether the configured SLSS uses the same configuration as Rel-12 D2D SLSS or not
Working assumption: No new synchronization signal sequence is defined in V2V

## Slide 3: Proposal
For the V2V PC5 SLSS:
  SLSS ID from GNSS timing can be defined by some reserved value(s) of the SLSS IDs:
    FFS: the detailed reserved value(s) of the SLSS IDs
    Notes: the reserved value(s) of the SLSS IDs can be (pre-)configured or pre-defined