## Slide 1: Way Forward on V2V PC5 timing
3GPP TSG RAN WG1 Meeting #84b R1-163710
Busan, Korea, 11th - 15th April 2016
Agenda Item: 7.3.2.4
Huawei, HiSilicon, ITRI, OPPO, CATR, Potevio, NEC, Nokia, ASB, Samsung, …

## Slide 2: Background
  There are agreements on the V2V sync:
  eNB instructs vehicle UE to prioritize either eNB-based synchronization or GNSS or GNSS-equivalent at least when the eNB is in the carrier where the vehicle UE operates on PC5 V2V
  GNSS or GNSS-equivalent is at the highest priority of synchronization source for time and frequency when the vehicle UE directly receives GNSS or GNSS-equivalent with sufficient reliability and the UE does not detect any cell in any carrier.

## Slide 3: Background
Observation:
  The timing of PC5 for V2V on the dedicated carrier can be decoupled from the eNB timing.
  It is beneficial for V2V PC5 to use a universal timing when the network is asynchronous.
    Reduce the packet missing or avoid additional time delay when multiple different timings received by a UE under the asynchronous network
  Note: the dedicated carrier means the eNB is not in the carrier where the vehicle UE operates on PC5 V2V

## Slide 4: Proposal
  A PC5 V2V uses a UTC timing when the eNB is not in the carrier where the vehicle UE operates on PC5 V2V
      PC5 V2V Frame Number (VFN) can be derived from the UTC timing
        FFS: how to derive the VFN