## Slide 1
Remaining Issues on Path Loss Scenarios
Theodore S. Rappaport, Shu Sun, George R. MacCartney Jr.
tsr@nyu.edu
May 8, 2016
 2016 NYU WIRELESS

## Slide 2
1. Path Loss Models for RMa Scenario
1. Existing ITU-R M.2135 RMa path loss model

## Slide 3
1. Path Loss Models for RMa Scenario
EXAMPLE: We ran current ITU path loss model using monte-carlo simulation (before the breakpoint). This example for 6 GHz.
KEY OBSERVATION: Existing RMa NLOS path loss model underestimates path loss well below free space value at close-in distances within 50 m, and has obvious errors (NLOS should be much lossier than free space) in first several hundred meters
For 6 GHz, CI model using n=2 (LOS) and n=2.8 (NLOS) predicts much more accurately for first several hundred meters at 6 GHz with same std. dev. and improved stability as shown for CI models, see:
http://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=7434656

## Slide 4
1. Path Loss Models for RMa Scenario
dBP (LOS breakpoint) is unrealistic and invalid for current model beyond approximately 14 GHz, and the model itself is only valid up to 10,000 m (Breakpoint is 10 km for ITU Rma model at 14 GHz!)
Cannot adopt Rma for mmWave in LOS! The breakpoint in ITU does not work!

## Slide 5
The existing RMa NLOS path loss model underestimates path loss below free space value at close-in distances (50 m), and is inaccurate and unrealistic up to 500 m (NLOS should have more loss than the model predicts).
1. Path Loss Models for RMa Scenario

## Slide 6
1. Path Loss Models for RMa Scenario
Simulation for best fit CI model was done using current ITU-R M.2135 RMa model at 1, 2, 6, 15, 28, 38, and 73 GHz using 1000 data points for each frequency, generated from monte-carol simulation. Different frequencies will yield smaller Std Dev for CI model as fit to the ITU-R M.2135 RMa model generated data. Note the problem with ABG model formula:
Much lower loss than free space when close to TX, a 4.86 dB Beta value is tens of dB less than 32.4 dB at 1 m FSPL. This makes no physical sense out to several hundred meters
Proposal:
a. Adopt CI NLOS model for RMa: PL(𝑓,𝑑)=27.8log10(𝑑)+32.4+20log10(𝑓), 𝜎=8.19 dB, d> 1m b. Adopt CI LOS model for RMa: PL(𝑓,𝑑)=20.5log10(𝑑)+32.4+20log10(𝑓), 𝜎=4.09 dB, d> 1m

## Slide 7
2. Dealing with Path Loss Transition Region
Path loss models that do not use a close-in free space reference have inaccuracies and difficulties predicting close-in distances, and are inaccurate at distances or frequencies different from those measured. For accuracy and stability issues, see: http://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=7434656
Using a transition model to fix a discontinuity at 6 GHz (2-10 GHz) GHz, without measured data and without addressing sensitivity issues, perpetuates inaccuracies
If we are going to the trouble to create a transition model without any data, why not consider a proven measurement-based model that works over all frequencies?
An optional way is to use the CI model that is based on measurements for the entire 2 orders of magnitude of frequencies (500 MHz - 100 GHz) for all scenarios
2. Proposal: Use an optional CI model for all scenarios instead of using transition

## Slide 8
UMa LOS Scenario:
CI:
UMa NLOS Scenario:
ABG:
CI:
UMi SC LOS Scenario:
CI:
UMi SC NLOS Scenario:
ABG:
CI:
UMi OS LOS Scenario:
CI:
UMi OS NLOS Scenario:
ABG:
CI:
3. Example of model inaccuracies using Results from White Paper
Note: f is in GHz and d is in meters. These forms are in 3GPP/ITU style.
K. Haneda et al., “5G 3GPP-like channel models for outdoor urban microcellular and macrocellular environments,” 2016 IEEE 83rd Vehicular Technology Conference (VTC Spring), May 2016. [Online]. Available: http://arxiv.org/abs/1602.07533.
K. Haneda et al., “Indoor 5G 3GPP-like channel models for office and shopping mall environments,” 2016 IEEE International Conference on Communications Workshops (ICCW), May 2016. [Online]. Available: http://arxiv.org/abs/1603.04079
much lower loss than free space when close to TX
much higher than free space loss with frequency

## Slide 9
3. Example of model inaccuracies using Results from White Paper
InH Office LOS Scenario:
CI:
InH Office NLOS Scenario:
Single-Slope Models:
ABG:
CIF:
InH Office NLOS Scenario:
Dual-Slope Models:
ABG:
CIF:
Note: f is in GHz and d is in meters. These forms are in 3GPP/ITU style.
K. Haneda et al., “5G 3GPP-like channel models for outdoor urban microcellular and macrocellular environments,” 2016 IEEE 83rd Vehicular Technology Conference (VTC Spring), May 2016. [Online]. Available: http://arxiv.org/abs/1602.07533.
K. Haneda et al., “Indoor 5G 3GPP-like channel models for office and shopping mall environments,” 2016 IEEE International Conference on Communications Workshops (ICCW), May 2016. [Online]. Available: http://arxiv.org/abs/1603.04079
See: http://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=7434656
much lower loss than free space when close to TX
much higher than free space loss with frequency

## Slide 10
3. Example of model inaccuracies Using Results from White Paper
InH Shopping Mall LOS Scenario:
CI:
InH Shopping Mall NLOS Scenario:
Single-Slope Models:
ABG:
CIF:
InH Shopping Mall NLOS Scenario:
Dual-Slope Models:
ABG:
CIF:
Note: f is in GHz and d is in meters. These forms are in 3GPP/ITU style.
K. Haneda et al., “5G 3GPP-like channel models for outdoor urban microcellular and macrocellular environments,” 2016 IEEE 83rd Vehicular Technology Conference (VTC Spring), May 2016. [Online]. Available: http://arxiv.org/abs/1602.07533.
K. Haneda et al., “Indoor 5G 3GPP-like channel models for office and shopping mall environments,” 2016 IEEE International Conference on Communications Workshops (ICCW), May 2016. [Online]. Available: http://arxiv.org/abs/1603.04079
See: http://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=7434656
much lower loss than free space when close to TX

## Slide 11
3. Example of model inaccuracies Using Results from White Paper
The currently approved 3gpp model has noticeable errors at close-in distances, i.e., it predicts much less path loss compared with free space. Optional close-in ref. distance does not have this issue
S. Sun et al., "Investigation of prediction accuracy, sensitivity, and parameter stability of large-scale propagation path loss models for 5G wireless communications," IEEE Transactions on Vehicular Technology, vol. 65, no. 5, pp. 1-18, May 2016. http://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=7434656

## Slide 12
3. Example of model inaccuracies Using Results from White Paper
The ABG model underestimates path loss at short distances, while overestimating path loss (i.e., underestimates interference) at large distances (e.g. 800 m) compared with the CI model
The CI/CIF model is more conservative when analyzing interference-limited systems at large distances and more realistic when modeling signal strengths at close-in distances.
S. Sun et al., "Investigation of prediction accuracy, sensitivity, and parameter stability of large-scale propagation path loss models for 5G wireless communications," IEEE Transactions on Vehicular Technology, vol. 65, no. 5, pp. 1-18, May 2016. http://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=7434656

## Slide 13
4. Proposal of Optional CI models for LOS and NLOS and all scenarios to solve inaccuracies and stability deficiencies
UMa LOS Scenario:
CI:
UMa NLOS Scenario:
CI:
UMi SC LOS Scenario:
CI:
UMi SC NLOS Scenario:
CI:
UMi OS LOS Scenario:
CI:
UMi OS NLOS Scenario:
CI:
RMa LOS Scenario:
CI:
RMa NLOS Scenario:
CI:
Note: f is in GHz and d is in meters. These forms are in 3GPP/ITU style.

## Slide 14
InH Office LOS Scenario
P
InH Office NLOS Scenario: Single-Slope Models:
InH Shopping Mall LOS Scenario:
InH Shopping Mall NLOS Scenario: Single-Slope Models:
Note: f is in GHz and d is in meters. These forms are in 3GPP/ITU style.
4. Proposal of Optional CI models for LOS and NLOS and all scenarios to solve inaccuracies and stability deficiencies

## Slide 15: Thank You!