## Slide 1: WF on URLLC Evaluation Scenario
Intel
3GPP TSG RAN WG1 Meeting #86 R1-168130
Gothenburg, Sweden, 22nd - 26th August 2016
Agenda item - 8.1.7

## Slide 2: Background
The assumptions of system level evaluation of URLLC NR are missed at the moment
It is proposed to consider at least sub 6 GHz Urban Macro single-layer layout and the corresponding parameters for evaluation of Urban Macro
  The medium inter-site distance of 500 meters allows to evaluate both noise-limited conditions and interference-limited conditions

## Slide 3: Proposal
Parameters | URLLC
Layout | Homogeneous hexagonal deployment with Macro-cell layer only as a baseline 57 cells
Inter-BS distance | 500 m
Carrier frequency | 4 GHz
Aggregated system bandwidth | 4 GHz: Up to 200 MHz (DL+UL)
Simulation bandwidth | Companies report
Channel model | 36.873 3D UMa
BS Tx power | Below 6GHz: 49dBm PA scaled down with simulation BW when system BW is higher than simulation BW. Otherwise, 49dBm
UE Tx power | 23 dBm
BS antenna configurations | See Table A.2.1-4. for Urban Macro
BS antenna height | 25 m
BS antenna element gain + connector loss | See Table A.2.1-4. for Urban Macro
BS receiver noise figure | 5 dB
UE antenna configurations | See Table A.2.1-4. for Urban Macro
UE antenna height | Following the modelling of TR36.873
UE antenna gain | 0 dBi
UE receiver noise figure | 9 dB
Traffic model | URLLC: FTP Model 1 or 3 with packet size 32-64 bytes and Poisson arrival rate. eMBB: Full buffer
Traffic load (Resource utilization) | FTP Model 1: Poisson packet arrival with arrival rate λ
UE distribution | Follow Urban Macro user distribution for both URLLC and eMBB UEs 20% Outdoor in cars: 30km/h, 80% Indoor in houses: 3km/h
BS receiver | Companies report, Baseline is MMSE-IRC
UE receiver | Companies report, Baseline is MMSE-IRC
Feedback assumption | Companies report, Part of design consideration
Channel estimation | Companies report, Practical channel estimation
Others | URLLC system outage is evaluated according to WF R1-168129