## Slide 1: WF on Initial Access for NR
AT&T, Ericsson
3GPP TSG RAN WG1 Meeting #87
Reno, USA 14th –18th November 2016
Agenda: 7.1.2
R1-1613141

## Slide 2: Background
From RAN1#86bis:
Agreements:
  From RAN1 specification perspective, NR air interface defines at least one periodicity of SS burst set
    FFS: whether or not to define common periodicity range for SS burst set across NR carriers
    Values of the periodicities of SS burst set is for further study
      E.g., 5ms, 40ms, 100ms
    The lowest value of the periodicity of SS burst set is X ms, e.g., 5ms, 40ms, 80ms
    Note: Interval of SS burst can be the same as interval of SS burst set in some cases, e.g., single beam operation
    Note: the main bullet can be applied to PSS, SSS and/or PBCH
  FFS: networks is allowed to transmit SS burst set at least at the defined periodicities
  FFS: UE is allowed or informed to adapt acquisition procedure based on periodicities of SS burst set
  FFS: For example, if multiple periodicities of SS burst set are defined for initial blind acquisition, UE assumes X ms of an NR carrier as periodicity of SS burst set for dwell time on a freq

## Slide 3: Motivation
A fixed transmission timing and frequency location of signals and channels related initial/random access is not desirable from a forward-compatibility perspective considering the introduction of future use cases or support for operating scenarios including LTE/NR coexistence

## Slide 4: Proposal
The time periodicity and frequency location for signals and channels related to initial/random access should be configurable by the network.
  FFS periodicity a UE assumes upon initial ‘blind’ cell search
  FFS signalling mechanism
  A given UE should only need to be configured and aware of the signals required for its own initial/random access and synchronization procedures.