## Slide 1: WF on Reference Signal for Demodulation
3GPP TSG RAN WG1 Meeting #87 R1-16xxxxx
Reno, USA, 14th – 18th November 2016
Agenda Item: 7.1.3.2
ZTE, ZTE Microelectronics, ASTRI, Samsung, Ericsson, Qualcomm

## Slide 2: Background
  Flexible demodulation RS design should be considered in NR MIMO which is suitable for various requirements/scenarios:
    E.g. for different frequency/scenarios/speeds
    E.g. for flexible Rx beam detection
    E.g. for different strengths/characteristics of phase noise
    E.g. for demodulation RS based RSRP/CSI-reporting
    E.g. for full/partial RS sharing between control and data(if needed)
    E.g. for different modulation orders
    E.g. for different service/traffic types
    E.g. for different resource allocation
    Other aspects are not precluded

## Slide 3: Proposal
  Support variable/configurable DMRS pattern for data demodulation
    FFS: Time and/or frequency domain density can be configured
    FFS: RE location can be configured
  Support multi-set DL DMRS for data demodulation
    The first set is front-loaded for demodulation
    Other set(s) can be configured for different motivations
      e.g. higher frequency/time density, Rx beam detection, RSRP/CSI-reporting, phase noise compensation
  FFS: multi-set UL DMRS for data demodulation