## Slide 1: Way Forward on 2os sPUSCH structure
Ericsson, Huawei, HiSilicon
R1-1613396
3GPP TSG RAN1 #87
Reno, Nevada (US), Nov 14 - 18, 2016
Agenda item 6.2.10.2.5

## Slide 2: Background
In RAN1#86 bis, a list of UL sTTI patterns was agreed for down-selection
It is preferable to have
  a sPUSCH pattern with fixed starting and end positions for data symbols to simplify the HARQ/scheduling timing related signaling
  a sPUSCH pattern not spanning over slot boundary to comply with intra-subframe frequency hopping based PUSCH resource allocation
  A sPUSCH pattern with the same structure in both slots of the subframe
  a sPUSCH pattern with a 3os sTTI at the end of the subframe to allow for data transmission in case of the presence of SRS

## Slide 3: Proposal
For 2-symbol TTI, the UL sTTI pattern for sPUSCH in OFDM symbols per subframe is (2, 2, 3, 2, 2, 3)
The data symbol(s) for sPUSCH are confined within a sTTI given by the above structure. Note that the DMRS for one sTTI may be placed within or outside the sTTI.
The presence (if any) and the position of the UL DMRS is given by the UL grant.
  If the UL DMRS is present it can be positioned before, within or after the sTTI
sTTI 1
sTTI 2
sTTI 0
sTTI 3
sTTI 4
sTTI 5