## Slide 1: WF on CSI-RS Resource Pooling Ericsson, LG Electronics, Huawei, Hi-Silicon, Samsung
3GPP TSG RAN1 #87 R1-1613504
Reno, USA, 14th – 18th November, 2016
Agenda Item: 7.1.3.3

## Slide 2: Background
From RAN1#86bis:
  Agreements:
  A CSI-RS resource set should be studied whereby CSI-RS resources within the set may be dynamically shared amongst users
  Study CSI-RS resources configuration in 2 steps
    Step 1: Pre-configure a set of K CSI-RS resources for one or more users through UE-specific RRC configuration
    Step 2: For a given user, dynamically indicate N out of K (where N >= 1) of the CSI-RS resources from the set to enable CSI measurement in a given time window
      Study the following alternatives
        Alt 1: Dynamic signaling through DCI
        Alt 2: Dynamic signaling through MAC CE
    The CSI-RS transmissions can be dynamically indicated as one shot or multi-shot within the window
    The configured CSI-RS resource pool can be used for channel/interference measurement
    Configure multi sets of CSI-RS resources for one UE

## Slide 3: Proposal
Support UE specific RRC configuration of one or more CSI-RS resource sets
  CSI-RS resources within a set can be dynamically shared amongst users
  Associaton of CSI-RS resources with TRP(s)/beam(s) should be transparent to the UE
Support dynamic allocation of one or more CSI-RS resources from the one or more sets to one or more users
  Allocation can be aperiodic (single-shot)
  Allocation can be on a semi-persistent basis
    De-allocation is dynamically signaled at a later point in time
    Note: semi-persistent CSI-RS transmission is periodic while allocated
Study the following aspects
  Signaling mechanism for dynamic allocation/de-allocation
    e.g. via MAC CE or L1 control signaling, via hierachical control signaling with MAC-CE and DCI
  Signaling mechanism for slot configuration (i.e., periodicity, subframe offset like in LTE)
  Signaling format for dynamic indication of CSI-RS resource(s)
  Signaling overhead reduction approaches
    e.g., structured groupings of CSI-RS resources and/or allocation scheme utilizing a combination of RRC configuration and dynamic signaling
  Methods to support resources of variable number of ports
    e.g. Aggregation of resources of a smaller number of ports