## Slide 1: WF on RS for Phase Tracking
Huawei, HiSilicon, Intel, National Instruments, ETRI, Samsung, LG Electronics, Ericsson, NTT DOCOMO, CMCC, InterDigital, Nokia, Alcatel-Lucent Shanghai Bell, Mitsubishi Electric, CATT, MediaTek, […]
3GPP TSG RAN WG1 Meeting #87 | R1-1613553
Reno, USA, 14 – 18 Nov 2016 | Agenda Item: 7.1.3.2

## Slide 2: Proposal
Phase tracking RS is denoted as PT-RS
PT-RS supports the following for CP-OFDM:
  Time-domain density of mapped on every other symbol and/or every symbol
    FFS: Whether/how to down-select the time-domain density
    Note: Other time-domain densities of PT-RS are not precluded
  At least for UL
    The presence of PT-RS is UE-specifically configured
      FFS: Whether implicit and/or explicit UE-specific configuration is supported
    PT-RS is confined in the scheduled time/frequency duration for a UE
  FFS: UE-specific and/or non-UE-specific and/or cell-specific for DL

## Slide 3: Proposal
The following are to be studied for PT-RS:
  Number of PT-RS ports to be supported
  Use of precoding
  QCL relationship with other RS, e.g., DM-RS
  Details on frequency domain pattern(s) and/or variable frequency domain densities
  Whether PT-RS is necessary for DFT-s-OFDM waveform
  Sharing of time/frequency resource between PT-RS among UEs and/or among layers of a single UE
  Additional usage for estimating residual frequency offset and/or high-speed channel
  Possible method(s) to improve phase estimation performance from PT-RS
    E.g., using ZP/NZP PT-RS to reduce interference
  Details of UE-specific configuration, e.g., associated with the scheduled MCS and/or BW, the number of scheduled layers, or use dedicated signaling
  Others are not precluded