## Slide 1: WF on power saving signal in NB-IoT
Huawei, HiSilicon,[….]
R1-1709371
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, May 15-19, 2017
Agenda item 6.2.7.1.1

## Slide 2: Background
In RAN1#88bis, an evaluation assumption was agreed and the following techniques are identified to be evaluated as the candidates for the power saving signal in NB-IoT:
Agreement:
    Techniques to be evaluated:
      Wake-up signal/channel (either relying or not relying on DL synchronization)
      Go-to-sleep signal/channel (either relying or not relying on DL synchronization)
      Compact DCI
      Dynamic USS periodicity
    The use of the technique can be semi-statically enabled/disabled by the network

## Slide 3: Proposals
At least for idle mode paging and connected mode DRX, specify a physical signal/channel that can be efficiently decoded or detected prior to decoding NPDCCH/NPDSCH for power saving;
  The power saving signal for the following cases can be further studied: General USS; Type2-CSS; Type2A-CSS
A power saving signal indicating wake-up is used for idle mode paging, and when the power saving signal is not detected prior to NPDCCH reception the associated NPDCCH decoding can be skipped by the UE
  NB-IoT downlink OFDM modulation is used
  FFS:
    Option 1: Wake-up/DTX transmission;
    Option 2: Always-on wake-up/go-to-sleep transmission;
  Working assumption: a NB-IoT UE is allowed to detect the power saving signal without prior synchronization at least for certain DRX/eDRX cycle range:
    FFS: the DRX/eDRX cycle range;

## Slide 4: Proposals
A power saving signal received/decoded prior to NPDCCH reception is used for connected mode DRX:
  FFS:
    Option 1: Wake-up/DTX transmission;
    Option 2: Always-on wake-up/go-to-sleep transmission;
    Option 3: Go-to-sleep/DTX transmission;
  NB-IoT downlink OFDM modulation is used