## Slide 1: WF on measurement based on SS block
NTT DOCOMO
3GPP TSG RAN WG1 Meeting #89 R1-1709412
Hangzhou, China
15th – 19th May, 2017
Agenda item: 7.1.1.5.1
Document for decision

## Slide 2: Background
Agreements:
Clarify previous RAN1 agreements on the RSRP definition for DL RRM measurements for L3 mobility as follows
  Define SS block RSRP and CSI-RS RSRP as
    SS block RSRP : measured RSRP from SSS
      FFS additional use of PBCH-DMRS for measurement
    CSI-RS RSRP : measured RSRP from CSI-RS in connected mode

## Slide 3: Background
Evaluation results of RSRP measurement accuracy from companies show that
  NR-SSS with sequence length 127 can provide required RSRP measurement accuracy with sufficient L1 measurement samples.
  Using DMRS for PBCH additionally could achieve required RSRP measurement accuracy with fewer L1 measurement samples, even in one-short measurement.

## Slide 4: Proposal
DMRS for NR-PBCH is used for DL based RRM measurement based on SS block for L3 mobility in addition to NR-SSS
  DMRS for NR-PBCH and NR-SSS have statically or semi-statically fixed power offset

## Slide 5: Merged proposal
Option 1:
  DMRS for NR-PBCH is always used for DL based RRM measurement based on SS block for L3 mobility in addition to NR-SSS
Option 2:
  DMRS for NR-PBCH can be optionally used for DL based RRM measurement based on SS block for L3 mobility in addition to NR-SSS up to UE implementation
Option 3 (?):
  DMRS for NR-PBCH is used for DL based RRM measurement based on SS block for L3 mobility in addition to NR-SSS according to NW configuration
RAN1 sends LS to RAN4 to ask evaluation and down selection on above options
DMRS for NR-PBCH and NR-SSS have statically or semi-statically fixed power offset

## Slide 6: Updated proposal
SS block RSRP is defined based on the antenna port used for PSS/SSS/PBCH/DMRS
  UE assumes that NR-PBCH and NR-SSS have statically fixed power offset
RAN1 will send LS to RAN4 after deciding DMRS design

## Slide 7: Offline outcome
SS block RSRP is defined based on the antenna port used for PSS/SSS/PBCH/DMRS
  UE assumes that NR-PBCH and NR-SSS have statically fixed power offset
  RAN1 will send LS to RAN4 after deciding DMRS design