## Slide 1: Way Forward on feD2D sidelink power control
3GPP TSG RAN WG1 Meeting #89 R1-1709428
Hangzhou, China 15th – 19th May 2017
Agenda Item: 6.2.9.2.3.3
Huawei, HiSilicon, Sony, KDDI, Intel

## Slide 2: Background
At RAN1#88bis meeting, the following agreement for feD2D was reached:
  Sidelink power control taking into account propagation characteristics between Relay UE and Remote UE is further studied
    Propagation characteristics can include sidelink pathloss, received signal quality, interference level etc.
    FFS details of sidelink power control operation
  Companies are encouraged to quantify gains of sidelink power control enhancements and provide more evaluation for the next meeting relative to R12 power control operation

## Slide 3: Proposal
For feD2D sidelink power control, the following is supported:
  The sidelink maximum transmission power both for relay UEs and remote UEs is determined by network
  The sidelink transmission power both for relay UEs and remote UEs can be determined by either network or relay UE
    FFS details
  Sidelink pathloss is taken into account to determine the sidelink transmission power
    FFS how to determine the sidelink transmission power from relay or remote UE sides