## Slide 1: WF on multi-sTTI scheduling
Ericsson, KT Corporation
R1-1709445
3GPP TSG RAN1 #89
Hangzhou, China, 15th - 19th May 2017
Agenda item 6.2.1.2.2.1

## Slide 2: Background
Multi-sTTI scheduling can reduce control overhead while providing the benefit of fast processing for sPDSCH and sPUSCH

## Slide 3: Proposal (1/2)
For a UE configured with 2os sTTI operation, multi-sTTI scheduling is supported
  Multi-sTTI scheduling is RRC configured
  When configured with multi-sTTI scheduling,
    The UE is expected to monitor the DCI for multi-sTTI scheduling in PDCCH and sTTI 3
    The UE is expected to monitor sDCI1 in sTTI 1, sTTI2, sTTI4 and sTTI5
  The sTTI(s) that can be scheduled with a DCI for multi-sTTI scheduling include at least the following options
    All sTTIs of slot 0
    All sTTIs of slot 1
    All sTTIs of the subframe
    sTTI0 if the DCI for multi-sTTI scheduling is sent in PDCCH or sTTI3 if DCI for multi-sTTI scheduling is sent in sTTI3

## Slide 4: Proposal (2/2)
  The format of the DCI for multi-sTTI scheduling is based on the format of sDCI0 with at least the following modifications
    A single HARQ process ID is included and corresponds to the first scheduled sTTI
      The HARQ process ID for the remaining scheduled sTTI is determined by the UE similarly as in eLAA.
    A RV field per scheduled sTTI
    A NDI field per scheduled sTTI
    A field for indicating DMRS positions
    Note: the MCS and resource allocation is the same for all scheduled sTTIs