## Slide 1: WF on Aperiodic CSI-RS Activation
Samsung, LG Electronics
3GPP TSG RAN WG1 89
Hangzhou, China, 15th - 19th May 2017
Agenda item: 7.1.2.3.1
R1-1709450

## Slide 2: Background
The following was agreed in RAN1#88bis:
  Study further activation mechanism (selecting N out of K NZP/ZP CSI-RS resources or resource sets, including joint trigger vs. separate triggers for resources, IMR, and/or reporting setting, reliability/latency associated with the activation, etc.) and the associated details (e.g., impact on DCI signaling, etc.) for aperiodic (AP) and semi-persistent (SP) CSI-RS
  Based on at least the supported number S of CSI-RS resource sets and number of CSI-RS resources Ks per resource set, agree to specify one or both of these options for aperiodic CSI-RS
    Option 1: use RRC + MAC CE + DCI
    Option 2: use RRC + DCI
When a UE is configured with multiple DL component carriers (CCs), the mapping between code points of the DCI field and the selected CSI-RS resource needs to be signalled to the UE

## Slide 3: Proposal
When a UE is configured with K NZP CSI-RS resources (resource sets) in a Resource setting (via RRC), the following activation mechanism is supported for AP-CSI-RS:
  When K ≤ Kmin or N ≤ Nmin, Option 2 is used
  Else, Option 1 is used
    MAC CE signalling includes the mapping between the code points of DCI field and the N activated CSI-RS resource(s) for each CC
FFS: Values of Kmin and Nmin