## Slide 1: On number of SS blocks
Nokia
3GPP TSG RAN WG1 Meeting #88bis
Hangzhou, P.R. China, 15th – 19th May 2017
Agenda: 7.1.1.1.3
R1-170xxxx

## Slide 2: Background
In RAN1#88bis following agreement was made
The considered maximum number of SS-blocks, L, within SS burst set for different frequency ranges are
  For frequency range up to 3 GHz, the maximum number of SS-blocks, L, within SS burst set is [1, 2, 4]
  For frequency range from 3GHz to 6 GHz, the maximum number of SS-blocks, L, within SS burst set is [4, 8]
  For frequency range from 6 GHz to 52.6 GHz, the maximum number of SS-blocks, L, within SS burst set is [64]
The way the value of L is reflected in specification is FFS
  Aforementioned values are to be used to facilitate the NR initial access design and evaluate the specification impact
  Possibility of having unified frequency agnostic signaling design is not precluded

## Slide 3: Discussion
In attempt to summarize views expressed in contributions following options could be identified
  The considered maximum number of SS-blocks, L, within SS burst set for different frequency ranges are
    For frequency range up to 3 GHz, the maximum number of SS-blocks, L, within SS burst set is [2 or 4]
    For frequency range from 3GHz to 6 GHz, the maximum number of SS-blocks, L, within SS burst set is [4 or 8]
    For frequency range from 6 GHz to 52.6 GHz, the maximum number of SS-blocks, L, within SS burst set is 64
How to reflect the L in the specification
  Option 1: Limit the possible time locations of SS block to L, which is the same as the maximum number of SS blocks in SS burst set
  Option 2: Allow over provisioning the possible time locations of SS block to L, but restrict the maximum of actually transmitted SS blocks to number to L
  FFS: other implications