## Slide 1: WF on transient period impact for PC5 operation with Short TTI
LG Electronics, Qualcomm
3GPP TSG RAN WG1 Meeting #89 R1-170xxxx
Hangzhou, China 15th – 19th May 2017
Agenda item: 6.2.3.3.1

## Slide 2: Background
Example of inter-carrier interference (ICI) caused by transient period of slot TTI channel (sTTI) to legacy TTI channel (nTTI) reception, when sTTI and nTTI are FDMed in the same subframe.

## Slide 3: Proposals
  The following impacts of transient period of short TTI (sTTI) should be taken into account for study and evaluation of PC5 operation with sTTI.
  Inter-carrier interference to legacy TTI (nTTI) reception when nTTI and sTTI are FDMed, which is caused by emission during the transient period at the sTTI boundary and right after the shared AGC symbol (if the shared AGC symbol operation is adopted)
  Symbol overhead for transient period of sTTI
  FFS on details of modeling for the evaluation