## Slide 1: WF on UL non-codebook based transmission
Huawei, HiSilicon, LGE, CATT, Ericsson, CeWiT, Deutsche Telekom, China Telecom, Xinwei, Tejas Networks, CATR, MediaTek, IITH, IITM
3GPP TSG RAN WG1 Meeting #89 R1-1709549
Hangzhou, China, 15 -19 May 2017
Agenda item – 7.1.2.1.4

## Slide 2: Background
Agreements in RAN1 meeting #88:
  NR supports UL-MIMO scheduling by DCI, which includes at least some of
    Indication of a SRS resource (SRI) which has been transmitted by this UE in previous time instance
      Each configured SRS resource is associated with at least one UL Tx beam/precoder
      FFS: whether to allow the existence of this field only when multiple SRS resources are configured to UE.
    Transmit Rank indicator (TRI)
      Possible values are up to the number of SRS ports configured in the indicated SRI
    Wideband transmit PMI (TPMI), with details FFS including dual-stage codebook (if supported)
      FFS: Possible PMs depend on the number of SRS ports configured in the indicated SRI
      FFS: whether to allow the existence of this field for non-codebook-based UL-MIMO transmission
      FFS: Subband TPMI
    UL MCS indication
    UL HARQ related information
    UL Resource allocation
    FFS on multiple SRI indication and corresponding indications of TRI(s) and TPMI(s)
    FFS: Joint encoding or separate encoding

## Slide 3: Proposal
For PUSCH precoder determination in non-codebook-based UL MIMO,
  At least support signalling of SRI(s) only, without TPMI indication in the UL grant.