## Slide 1: WF on CSI-RS based RRM measurements on detected cells
ZTE, …
3GPP TSG RAN WG1 Meeting #89
Hangzhou, USA, 15th – 19th May 2017
Agenda: 7.1.1.5.2
R1-170xxxx

## Slide 2: Background
In R1-1709061, RAN2 asked about the option that UEs can derive the CSI-RS for RRM measurements for L3 mobility from the cell IDs of detected cells.
This is related to the concept of listed cells and detected cells in LTE measurements [36.331]:
The measurement procedures distinguish the following types of cells: 1. The serving cell(s) - these are the PCell and one or more SCells, if configured for a UE supporting CA. 2. Listed cells - these are cells listed within the measurement object(s) or, for inter-RAT WLAN, the WLANs matching the WLAN identifiers configured in the measurement object or the WLAN the UE is connected to. 3. Detected cells - these are cells that are not listed within the measurement object(s) but are detected by the UE on the carrier frequency(ies) indicated by the measurement object(s). For E-UTRA, the UE measures and reports on the serving cell(s), listed cells, detected cells and, for RSSI and channel occupancy measurements, the UE measures and reports on any reception on the indicated frequency.

## Slide 3: Background
One mode of operation is that a UE performs CSI-RS based RRM measurements only on detected cells for which it has obtained an explicit configuration ("only listed cells").
In some scenarios, inter-gNB coordination is limited and neighbor relations are not available/accurate, for example unlicenced and early deployments.
It is useful to support a mode of CSI-RS based RRM measurements on a particular carrier frequency configured by dedicated RRC signaling where:
  Some CSI-RS configuration parameters, e.g. RS sequence, are derived from the cell ID of a detected cell.
  Other CSI-RS configuration parameters are based on a carrier frequency specific configuration (fixed in spec or configurable)
Note that this does not impose that the CSI-RS are always on. A UE can blindly detect or measure the CSI-RS of a detected neighbor cell.
A configuration derived from cell ID and carrier frequency could be overridden by a UE-specific configuration for the detected cell.

## Slide 4: Example
Mode 1 (no CSI-RS for L3 mobility): RRM measurements only on IDLE mode RS
Mode 2 (only listed cells): If the UE has an explicit CSI-RS configuration for the detected cell (i.e. listed cell), the UE measures/reports it.
Mode 3 (listed and detected cells): The CSI-RS configuration of a (non-listed) detected cell is derived from cell ID and frequency specific configuration.
carrier frequency f1
carrier frequency f2
carrier frequency f3
UEs in serving cell on f1
Mode 2 on f1: UEs measure
CSI-RS only on cells with
explicit CSI-RS configuration
(only listed cells)
Mode 3 on f3: UEs can obtain
CSI-RS configuration from cell ID
and frequency specific config
(listed and detected cells)
Mode 1 on f2: UEs measure
and report only only IDLE RS

## Slide 5: Proposal
A UE can be configured to perform RRM measurements on a carrier frequency according to at least the following modes:
  Mode 1:
    RRM measurement and reporting only based on IDLE mode RS
  Mode 2:
    RRM measurement and reporting based on IDLE mode RS.
    CSI-RS based RRM measurement and reporting only on listed cells
  Mode 3:
    RRM measurement and reporting based on IDLE mode RS.
    CSI-RS based RRM measurement and reporting on listed cells and detected cells
A UE can be configured with different modes on different carrier frequencies
A listed cell is a cell that is configured as timing reference in a CSI-RS configuration.
A detected cell is detected but not listed.
In mode 3, the CSI-RS configuration of a detected cell can be obtained as follows:
  Part A of the CSI-RS configuration can be derived from the cell ID (of the detected cell).
  Part B of the CSI-RS configuration can be configured for the carrier frequency.
  Part C of the CSI-RS configuration is fixed.
  FFS Parameters, if any, included in parts A, B and C.
Note that in mode 3, the explicit configuration of a listed cell overrides the derived configuration
Note that the number of listed cells in mode 3 could be zero.
Note that using mode 3 on a carrier frequency does not imply that the CSI-RS is always on.