## Slide 1: Outcome of the offline discussion on UL partial subframes
Nokia
3GPP TSG RAN WG1 Meeting #89 R1- 1709585
Hangzhou, P.R. China 15th – 19th May 2017
Agenda item: 6.2.2.2

## Slide 2: Background
In RAN1#88bis the following was agreed:
Agreement:
At least one additional UL ending point is introduced
The ending point is indicated with a UL grant allocating the resources for the subframe
Agreement:
At least one additional UL starting point is introduced
FFS: details, including whether the starting point is indicated with an UL grant or not

## Slide 3: Proposal (1)
UL partial subframe transmission starting at symbol #7 is supported with both following modes Mode 1 and Mode 2
Mode 1. The UE may start at a Rel-14 starting point or at symbol #7 depending on e.g. the outcome of LBT
  The TBS is determined as for the full subframe regardless of the starting point (i.e. no TBS scaling)
  FFS between:
    When transmission starts at symbol #7, the first slot of a subframe is punctured
    When transmission starts at symbol #7, the TB(s) is rate matched into the second slot
  FFS: channel access within shared COT
  FFS: whether and how to indicate to which UL subframes this applies
Mode 2. The UL grant indicates starting position at number #7
  FFS: additional starting points between symbols #7 and #8
  The TB(s) is rate matched into the second slot
  FFS: TBS determination (e.g. TBS scaling, or puncturing)

## Slide 4: Proposal (2)
UL partial subframe transmission ending in the end of symbol [#3], #6, [#10] is supported
  FFS: other ending positions
  The ending position is indicated with the UL grant
  The TB(s) is rate matched into the allocated symbols
  FFS: TBS scaling
  FFS: UCI mapping, if supported
  FFS: whether the starting symbols is always #0 or as in Rel-14
  SRS transmission is not supported in these cases