## Slide 1: NR PRACH Preamble Design with Multiple Different ZC Sequences
CATT, Huawei, HiSilicon
3GPP TSG RAN WG1#89 R1-1709589
Hangzhou, China, 15th - 19th May 2017

## Slide 2: Background - I
In RAN1# 88bis, the following agreements were made on the NR RA preamble design:
  For RACH capacity enhancements,
    Option 2 with/without OCC and/or option 4 with different sequences can be considered
      Note: for option 4, combination with different sequences can be studied
      Note: for option 4, two-stage or multiple-stage UE detection can be studied for possible complexity reduction for PRACH detection

## Slide 3: Background - II
In RAN1# 89, Option 4 was further studied, which shows the following advantages:
  Option 4 with multiple different ZC sequences can significantly increase the PRACH capacity in term of the number of PRACH preamble sequence with the same time/frequency resource in comparison with other options
  Option 4 with multiple different ZC sequences is more robust to frequency offset in comparison with one ZC sequence preamble

## Slide 4: Proposal
NR supports PRACH preamble design composed with multiple different ZC sequences.