## Slide 1: Harmonized proposal for CBG and preemption indication
NTT DOCOMO, INC., ZTE, Sharp, Ericsson, KT Corp., Samsung, Huawei, HiSilicon, Sony, InterDigital, MediaTek, Fujitsu, Intel, Panasonic, Nokia, ASB, OPPO, CATR, CATT
R1-1709602
3GPP RAN1 #89
Hangzhou, P.R. China
15th – 19th May 2017
7.1.3.3.5

## Slide 2: Harmonized proposal for downlink
Both are supported for Rel.15 NR.
For DL CBG-based (re)transmission,
  Following information can be configured to be included in the same DCI:
    Which CBG(s) is/are (re)transmitted.
    Which CBG(s) is/are handled differently for soft-buffer/HARQ combining.
      FFS: whether/how UE behavior is specified, e.g., part/whole of soft-buffer of indicated CBG(s) is flushed.
  FFS: timing of CBG-based (re)transmission.
For preemption indication;
  When configured, the indication tells the UE(s) which DL physical resources has been preempted.
  The preemption indication is transmitted using a PDCCH.
    The preemption indication is not included in the DCI that schedules the (re)transmission of the data transmission.
  FFS: the granularity of the time and/or frequency resources.
  FFS: what DCI is used.
  FFS: timing of the preemption indication.