## Slide 1: WF on CSI-RS design for beam management
Samsung, Intel, KT, Ericsson
R1-1709617
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, 15 – 19 May 2017
Agenda item 7.1.2.4.1

## Slide 2: Proposals
A resource unit is defined as a set of CSI-RS antenna ports which comprises of NP x L REs in an OFDM symbol
  NP is the number of antenna ports in a resource unit.
  Antenna port index is defined within a resource unit
  If IFDMA is supported for sub-time unit partitioning method, L > 1 and some of REs in the set can have zero transmit power. For other sub-time unit methods, L = 1.
Based on a gNB’s configuration, a BW for CSI-RS can be used only for CSI-RS in an OFDM symbol for the beam management purpose
  K resource units respectively associated with CSI-RS resources indexed by 0, 1, …, K-1 are cyclically and continuously mapped on the REs within the configured BW in that OFDM symbol
  FFS: RE mapping for antenna ports within a resource unit (e.g. FDM or CDM), Configuration parameter details

## Slide 3: A resource unit is defined as a set of CSI-RS antenna ports which comprises of NP x L REs in an OFDM symbol
Note: if IFDMA is used for sub-time unit partitioning method, L > 1 and some of REs in the set can have zero transmit power. For other sub-time unit methods, L = 1.
`

## Slide 4
`
  K resource units associated with CSI-RS resources indexed by 0, 1, …, K-1 are cyclically and continuously mapped on the REs within the configured BW in that OFDM symbol

## Slide 5: Based on a gNB’s configuration, a configured BW can be used only for CSI-RS in an OFDM symbol for the beam management purpose
: K resource units