## Slide 1: Way Forward on Group-based Beam Reporting
Intel, Ericsson, CATT, MediaTek, Xinwei
3GPP TSG RAN WG1 Meeting #89 R1-17xxxxx
Hangzhou, China 15th – 19th May 2017
Agenda Item: 7.1.2.2.1

## Slide 2: Background
In the previous meetings, the following agreements have been achieved on group-based beam reporting
  Alt 1:
    UE reports information about TRP Tx Beam(s) that can be received using selected UE Rx beam set(s) where a Rx beam set refers to a set of UE Rx beams that are used for receiving a DL signal.
    NOTE: Different TRP Tx beams reported for the same Rx beam set can be received simultaneously at the UE.
    NOTE: Different TRP TX beams reported for different UE Rx beam set may not be possible to be received simultaneously at the UE
  Alt 2:
    UE reports information about TRP Tx Beam(s) per UE antenna group basis where UE antenna group refers to receive UE antenna panel or subarray.
    NOTE: Different TX beams reported for different antenna groups can be received simultaneously at the UE.
    NOTE: Different TX beams reported for the same UE antenna group may not be possible to be received simultaneously at the UE

## Slide 3: Proposal
For beam management with beam group reporting, the number of groups M and the number of Tx beams per group N can be UE-specifically configured
  Configuration of M = 1 and N = 1 are supported which implies no impact to reporting and indication overhead
  The UE specific configuration can be based on UE capability
  Decide the maximum values of M, N supported by the spec in the next meeting to be able to determine impact on reporting and indication overhead
  Down-selection between Alt1 and Alt2 at next meeting
  FFS: The number of groups reported could be smaller than M and the number of Tx beams reported per group could be smaller than N
  FFS: Companies are encouraged to evaluate performance to determine maximum values of M,N for the first release of NR