## Slide 1: On uplink power control for Rel-13 NB-IoT
3GPP TSG RAN1 Meeting #89 DRAFT_R1-1709672
Hangzhou, China, May 15-19, 2017
Agenda Item: 6.1.1
Source: Huawei, HiSilicon
Document for: Discussion and decision

## Slide 2: R13 uplink power control
For NPRACH, the UE selects the NPRACH resource coverage level by NRSRP measurement.
If the selected level is level 0, UE transmit power is calculated by path-loss which is derived based on NRSRP measurement
Otherwise (in level 1 and level 2) UE transmits at maximum configured power

## Slide 3: Problems of R13 uplink power control
UE2, cell center
frequency
power
UE2
UE1
If the UE2 in cell center fails to access the network with NPRACH level 0, UE2 changes to NPRACH level 1, and transmits NPRACH with configured maximum power, which blocks other cell edge UEs.
UE1, cell edge
NPRACH
power
-20dBm
23dBm
A large power ramp when switching to coverage class1

## Slide 4: It is impossible to prevent a center UE using NPRACH level 1
If NPRACH resource in level 0 is limited, NPRACH collisions mean some cell center UEs in level 0 (close to eNB) will eventually transmit at maximum power on NPRACH resource for level 1
If there is strong DL interference, RAR may not be received by a coverage level 0 UE, which will eventually cause the UE to move into level 1, and transmit with maximum power
Either case will raise the interference level at eNB, due to the potentially large path loss differences between UEs

## Slide 5: Suggested example solution to high interference after NPRACH level change
SOLUTION: eNB signals if it supports an updated RACH power control procedure to use the level 0 power control method in all NPRACH levels, i.e. based on path-loss with power ramping
  UE can (optional) use the updated RACH power control if it has implemented it (optional)
  Backward compatible Rel-13 CRs
  Affected specifications
    36.213: NPRACH power control
    36.321: NB-IoT RACH power ramping
    36.331: Signaling
PROPOSAL 1: RAN1 agrees to select the exact solution and prepare CRs for RAN#76 by email discussion, and to request the same in RAN2

## Slide 6
Thank You
www.huawei.com