## Slide 1: WF on Processing Time Requirements
Qualcomm, ZTE, Ericsson, Deutsche Telekom
R1-1709696
3GPP TSG RAN WG1 #89
Hangzhou, China ,15th - 19th May 2017
Agenda item 7.1.3.3.4

## Slide 2: Background
RAN1 #86bis
Agreements:
For slot-based scheduling, NR specification should support the following
  DL data reception in slot N and corresponding acknowledgment in slot N+K1
    All UEs should support K1≥1 with exact values for K1 FFS
    Some UEs may support K1=0 (FFS conditions)
  UL assignment in slot N and corresponding uplink data transmission in slot N+K2
    All UEs should support K2≥1 with exact values for K2 FFS
    Some UEs may support K2=0 (FFS conditions)

## Slide 3: Proposal
For NR Release 15
  Mandatory UE support of self-contained operation (K1=0 and K2=0), at least for up to 30kHz numerology

## Slide 4: Background

## Slide 5: Low Latency
Reduces TxOp delay for both 1st Tx and Re-Tx (single-interlace HARQ)
4G LTE TDD
5G NR TDD*
1 ms
Sub 6 GHz, macro cell numerology
30 kHz tone spacing
OTA latency is impacted by transmission duration and UE/network response time
NR has shorter control/data transmission time: 10’s of usec compared to LTE 1ms
NR self-contained subframe allows UE to respond within 10’s usec compared to LTE > 4ms
Latency reduction by 10x
Reference: R1-1708629, “Processing Time Requirements”

## Slide 6: Forward Compatibility -1/2
4G LTE
TDD
5G NR
TDD*
* Sub 6 GHz, macro cell numerology, 30 kHz tone spacing
Not Forward
Compatible
PDCCH <->UL data
UL data <-> PHICH
PDSCH <-> ACK
ACK <-> ReTx
Constrained Forward
Compatibility
Self-contained subframe removes subframe inter-dependency
Reference: R1-1708629, “Processing Time Requirements”

## Slide 7: Forward Compatibility -2/2
Self-contained SF:
  Option 1: No scheduling in slot n+1
  Option 2: Indicator channel at slot n+1 signals blanked slot
  Option 3: Signaling at slot n
    Decision to be made before slot n
Non-Self contained SF:
  Signaling at slot n
    Blanking decision to be made “k” subframes ahead depending on UE capability
    Similar to LTE TDD inter-dependency shown in previous slide
      Slot n DL data to be ACK’ed at the next un-blanked slot after k
      UL grant sent at slot n applicable for the next un-blanked slot after k
    Example k = 2
Blank resources in slot n+1
Blanked Resource
Slot n
Slot n+1
Blanked Resource
Slot n
Slot n+1
SCSF
DL
nSCSF
DL,
nSCSF
UL,
Blanked Resource
Slot n
Slot n+1
SCSF
UL
Reference: R1-1708629, “Processing Time Requirements”

## Slide 8: SCSF operation for link budget
UE capability for SCSF also allows immediate acknowledgement w/in next long uplink bursts

## Slide 9: Background
RAN1 #85
Agreements:
NR design should strive at least to enable the possibility for
  Corresponding acknowledgement reporting shortly (in the order of X µs) after the end of the DL data transmission
  Corresponding uplink data transmission shortly (in the order of Y µs) after reception of UL assignment
  Note: may depend on e.g. UE capability/category, payload size, etc
  FFS: X and Y in the order of a few tens of or hundreds of micro sec is feasible
Other mechanisms/configurations in addition to fast/short corresponding acknowledgement are needed
  For example to provide coverage or enable TD-LTE coexistence
Note: RAN1 will continue investigations about UE complexity, implementation processing time, interleaving applicability

## Slide 10: Background
The following are some agreed-upon terminology to provide context:
  K0: Delay between DL grant and corresponding DL data (PDSCH) reception
  K1: Delay between DL data (PDSCH) reception and corresponding ACK transmission on UL
  K2: Delay between UL grant reception in DL and UL data (PUSCH) transmission
  K3: Delay between ACK/NAK reception in UL and corresponding retransmission of data (PDSCH) on DL