## Slide 1: WF on assignment for DL and UL transmission
CMCC
3GPP TSG RAN WG1 #89 Meeting R1-1709795
Hangzhou, P.R. China, 15th – 19th May 2017
Agenda item: 7.1.3.1.5

## Slide 2: Background
RAN1#88bis
Agreements:
From UE signaling perspective,
  The higher layer signalling for the semi-static assignment of DL/UL transmission direction for NR can achieve at least the followings
    A periodicity where the configuration applies;
      FFS: Detailed periodicity set;
      FFS: how to achieve the signaling of periodicity
    A subset of resources with fixed DL transmission;
      FFS: The subset of resources can be assigned in granularity of slot and/or symbol;
    A subset of resources with fixed UL transmission;
      Resources with fixed UL transmission happens in the ending part of the periodicity is supported;
      FFS: The subset of resources can be assigned in granularity of slot and/or symbol;
  FFS: Other resources not indicated as “fixed UL” or “fixed DL” or “reserved/blank” can be considered as “flexible resource”, where transmission direction can be changed dynamically.

## Slide 3: Proposal
Regarding to the periodicity that included in the higher layer signalling for the semi-static assignment of DL/UL transmission direction for NR, at least the following values are supported:
  roughly 0.125ms, roughly 0.25ms, 0.5ms, 1ms, 2ms, 5ms, 10ms;
    Each periodicity is supported for particular SCS(s)/slot duration(s)
      FFS: details