## Slide 1: WF on Front-load DMRS design
3GPP TSG RAN WG1 Meeting #89 R1-1709833
Hangzhou, China, 15th – 19th May, 2017
Agenda Item: 7.1.2.4.2
Qualcomm, Huawei, HiSilicon, ZTE, Mediatek, Ericsson, [Nokia], Mitsubishi, LGE, ITL, Docomo, ETRI, CATT, [Samsung]

## Slide 2: Proposal
  UEs in a cell are higher layer configured with 2 DMRS configurations for the front-load DMRS for UL/DL CP-OFDM
  Front-load DMRS Configuration 1: Supports up to 8 ports
    IFDM based pattern with Comb [2] and/or [4] w cyclic shifts (CS)
      One OFDM symbol:
        To be down selected to 1 Alt:
          Alt 1: Comb 2 + 2 CS, up to 4 ports
          Alt 2: Comb 4 + 2 CS, up to 8 ports
      Two OFDM symbols:
        To be down selected to 2 Alts:
          Alt. 1: Comb 2 + 2 CS + TD-OCC ({1 1} and {1 -1}), up to 8 ports
          Alt. 2: Comb 2 + 4 CS + TD-OCC ({1 1}), up to 8 ports
          Alt. 3: Comb 4 + 2 CS + TD-OCC ({1 1}), up to 8 ports
  Front-load DMRS Configuration 2: Supports up to 12 ports
    FD-OCC pattern with adjacent REs in the frequency domain
      One OFDM symbol:
        To be down selected to 1 Alt:
          Alt. 1: 2-FD-OCC across adjacent REs in the frequency domain up to 6 ports
          Alt. 2: 2-FD-OCC across adjacent REs in the frequency domain up to 4 ports
      Two OFDM symbols:
        2-FD-OCC across adjacent REs in the frequency domain + TDM up to 12 ports
        2-FD-OCC across adjacent REs in the frequency domain + TD-OCC (both {1,1} and {1,-1}) up to 12 ports
  FFS: DMRS pattern before configuration, e.g., SIB1
Notes: i