## Slide 1: WF on eNB to UE COT sharing in Autonomous UL in FeLAA
CableLabs, Broadcom, Comcast, HPE
Charter Communications, Brocade, Blackbery
3GPP TSG RAN WG1 Meeting #91 R1- 1721076
Reno, Nevada, 27th Nov – 1st Dec 2017
Agenda item: 6.2.2.2.3

## Slide 2: Background
The intent for introducing a shared and paused COT for Release 14 LAA and also in ETSI-BRAN was to only account for the grant-to-transmission delay in scheduled UL. So, in principle a shared and paused COT should not be used for AUL (autonomous UL).
However, if it is used for AUL, fair coexistence aspects must be considered; also by ensuring that multiplexing of data of different channel access categories is in line with the principles and agreements in LAA Release 13 DL and Release 14 UL.

## Slide 3: Proposal
The following must be considered to ensure that the UE transmits data of the appropriate priority class in the shared COT. In this case, since there is no explicit grant from the eNB, it is for the AUL UE to ensure that the LBT priority class to traffic type map and the corresponding traffic multiplexing rules are followed (as is the case for Type 1 AUL channel access). The conditions are as follows:
  For autonomous UL transmission based on 25 us LBT, the channel access priority class is indicated by the eNB.
  The UE will use the LBT priority class to traffic type mapping defined for LAA Rel-13 [36.300 section 5.7.1]
  The multiplexing of data by the UE shall follow the corresponding eNB operation when transmitting DL data in a COT as specified in LAA Rel-13 [36.300 section 5.7.2]