## Slide 1: Way Forward on configuration of power saving signal for IDLE mode paging
Huawei, HiSilicon, ….
3GPP TSG RAN WG1 Meeting #91
RENO, USA, 27 November – 1 December 2017
Agenda item 6.2.6.1.1.2
R1-1721182

## Slide 2: Background
In RAN1#90bis, it was agreed:
Agreements:
RAN1 assumes that introduction of WUS does not alter PO/PF definition
At least in a UE’s DRX cycle:
  WUS supports at least being applied to all the UEs monitoring WUS associated to a PO in a cell NB-IoT carrier;
    FFS: eNB can configure WUS being applied to a group of more than one of the UEs associated to a PO in a cell NB-IoT carrier
    Send LS to request RAN2 input on feasibility of UE groups for WUS. (Xiaolei, HiSilicon, prepare draft LS in R1-1719102)
Working assumption:
At least in a UE’s DRX cycle, how the UE knows the WUS time location, is:
  A WUS has a time location which is configurable with respect to the associated PO(s) location(s)
Agreements:
At least in a UE’s DRX cycle, one WUS informs UE whether to monitor the PO in a single DRX cycle
Include in the LS to RAN2, to request input on the feasibility of WUS applying to more than one PO in a PTW for eDRX case

## Slide 3
Proposals:
Confirm the working assumption: Working assumption:
  At least in a UE’s DRX cycle, how the UE knows the WUS time location, is:
    A WUS has a time location which is configurable with respect to the associated PO(s) location(s)
The maximum duration of WUS is configured carrier specifically, and WUS actual transmission duration can be shorter than the configured maximum duration of WUS.
  Alt 1: The actual WUS duration is transmitted aligning to the start of the configured maximum duration of WUS.
  Alt 2: The actual WUS duration is transmitted aligning to the end of the configured maximum duration of WUS.
A gap from the end of configured maximum WUS duration to the associated PO is defined, and FFS if it is fixed or configurable.