## Slide 1
3GPP TSG RAN WG1 Meeting #92 R1-1801351
Athens, Greece, Feb.26 – Mar. 2, 2018
Agenda Item:7.1.7
Views on UE feature list
Huawei, HiSilicon

## Slide 2: Overview of RAN1-led NR features
0. subcarrier spacings
      60kHz[0-9] mandatory
1. Initial access and mobility
        CSI-RS based RRM/RLM mandatory [1-5, 1-7, 1-8]
2. MIMO/RS
        DMRS configuration type 2 [2-10, 2-17]
        Type 2 Codebook [2-41]
        SRS antennas switching [2-55]
3. UL/DL ctrl. , scheduling and HARQ
    PDCCH monitoring [3-5]
  UE Processing Time [5-5,5-6]
  Grant-free type I mandatory [5-13/14, 5-19]
  TDD operation in NR [3-6/5-1]
4. CA/DC, BWP, SUL
      Basic BWP and BWP adaptation [6-1/2/3/4]
      SUL and UL sharing [6-15/16/17/18/19]
  *The feature numbers are according to R1-1801289, “Rel-15 NR UE feature list”

## Slide 3: Subcarrier spacing

## Slide 4: Mandatory: 60kHz [0-9]
Benefits of 60KHz
For URLLC
  60kHz numerology can allow for relaxed
  hardware processing to meet 0.5ms URLLC
  latency than 30 kHz numerology
  60kHz can provide better performance (2-3dB) than 30kHz with the same mini-slot length
For eMBB
  Better (3-5dB) link performance for high speed scenario
  Better (12-16%) user throughput gain for low to medium traffic load
  60kHz agreed as mandatory for mm-wave, it is straight forward to support 60kHz for those UE which support mm-wave
URLLC coexistence with eMBB
  In a carrier, URLLC traffic can be flexibly scheduled in 60kHz BW part
    60kHz numerology provides more flexible scheduling opportunity for URLLC
    60kHz BW part does not contain SSB, hence, resource allocation is less constrained
  Regular/Large eMBB traffic can be scheduled in 30kHz or 15kHz BW part with slot-level TTI
  For dynamic resource sharing, eMBB traffic can be opportunistically scheduled in 60kHz BW part
Forward compatibility issues:
- If NR does not support 60kHz SCS, forward compatibility issues would occur for URLLC, eMBB, URLLC and eMBB coexistence
*Reference: R1-1801783

## Slide 5: IAM: CSI-RS based RRM/RLM mandatory

## Slide 6: Mandatory: CSI-RS based RRM/RLM [1-5,1-7,1-8]
NR Cell 1
NR Cell 2
UE movement
CSI-RS based mobility
After hand-over, network can immediately establish UE-specific TRP(s) for data communication
CSI-RS can be configured in wider bandwidth “as needed”, providing improved RSRP accuracy.
R1-1802081, Discussion on CSI-RS based RRM/RLM as a mandatory feature in Rel-15
CSI-RS for RRM and RLM is essential for good system performance
    Per UE CSI-RS can be configured in wider bandwidth and on a per need basis providing improved RSRP and RSRQ accuracy.
    Provide an accurate RLM(hypothetical PDCCH BLER) i.e. CSI-RS can be sent in narrower beam compared to SS-RS for RLM.
    Efficient for NR deployment supporting multi-TRPs per cell when SSB beams from different TRPs are transmitted on the same resources. Target cell can establish the right TRP(s) based on the CSI-RS association with RACH preamble.
    Allow networks to configure SS Blocks burst set periodicity up to 160ms for power efficient network operations.
    CSI-RS needs to be configured in Scells without SSB for efficient secondary carrier activation/deactivation, e.g. in non-contiguous intra cell CA.

## Slide 7: MIMO/RS

## Slide 8: Overview of MIMO/RS
4 layer PDSCH reception at the UE as mandatory [2-3]
PRB bundling with size 2/4 as mandatory [2-11]
DMRS configurations with up to 12 orthogonal ports as mandatory [2-10, 2-17]
  Support both configurations type 1 and type 2
2 layer PUSCH transmission at the UE as mandatory [2-12]
CSI-RS based beam management as mandatory [2-24]
DL Codebook: Type-I up to 16 ports and a subset of Type II feedback schemes as mandatory [2-36/41]
PTRS as mandatory at least for high frequency [2-44/47]
CSI-RS for fine time and frequency tracking (TRS) as mandatory [2-50]
SRS antenna switching and carrier-based switching as mandatory [2-55/56]

## Slide 9: Mandatory: DMRS configuration type 2 [2-10, 2-17]
 | DMRS configuration Type 1 | DMRS configuration type 2
Main Features | Max 8 orthogonal ports for MU Max 4/8 ports for DL SU Comb 2 + 2 CS + (TD-OCC) | Max 12 orthogonal ports for MU Max 6/8 ports for DL SU 2-FD-OCC across adjacent REs + (TD-OCC)
Throughput | Lower throughput performance Smaller number of ports | Higher throughput performance Larger number of ports 15%~20% mean UPT gain for 4Rx UE and 17%~29% mean UPT gain for 8Rx UE
Estimation Performance | Poor performance due to de-spreading loss: Performance loss compared to type 2 DMRS for large subcarrier spacing scenarios Performance loss compared to type 2 DMRS for frequency-selective scenarios | Robust performance with higher de-spreading gain: Benefit to large subcarrier spacing scenarios Benefit to frequency-selective scenarios ~1dB SINR gain @60KHz SCS or 1000ns delay spread
Reception Complexity | Higher channel estimation complexity Limits PRB bundling size | Lower channel estimation complexity Can support larger bundling size

## Slide 10
Mandatory: Type 2 Codebook [2-41]
Comparison between type I and type II
Table 1 |  | 
Items | NR Type I | NR Type II
Principle of codebook design | beam selection codebook | Beam combination codebook
Feedback overhead | See the table 2 | 
performance | See the table 3-4 | 
Supported rank | Rank 1~8 | Rank 1~2
Table 2. Overhead comparison |  |  |  |  |  |  | 
Payload size for 4 ports |  |  |  |  |  |  | 
 | Type I |  |  |  | Type II (L=2,W+S,8PSK) |  | 
 | WB-reporting | SB-reporting (10 subbands) |  |  | WB-reporting | SB-reporting (10 subbands) | 
Rank 1 | 5 | 23(L=1)/42(L=4) |  |  | 24 | 135 | 
Rank 2 | 6 | 15(L=1)/34(L=4) |  |  | 44 | 266 | 
Payload size for 8 ports (wideband) |  |  |  |  |  |  | 
 | Type I |  | Type II (L=2, W+S,8PSK) |  | Type II (L=3, W+S,8PSK) |  | Type II (L=4, W+S,8PSK)
Rank 1 | 8 |  | 27 |  | 39 |  | 49
Rank 2 | 9 |  | 47 |  | 72 |  | 94
Payload size for 8 ports (10 subbands) |  |  |  |  |  |  | 
 | Type I |  |  | Type II (L=2, W+S,8PSK) | Type II (L=3, W+S,8PSK) |  | Type II (L=4, W+S,8PSK)
Rank 1 | 26(L=1)/45(L=4) |  |  | 138 | 184 |  | 268
Rank 2 | 18(L=1)/37(L=4) |  |  | 269 | 362 |  | 532
Table 3. Performance of 4T2R |  |  |  |  | 
CSI Type | config | Amp. | Phase | Avg Gain (MB) | Edge Gain (MB)
NR Type I | config1 |  |  | 0.00% | 0.00%
 | config2 |  |  | 1.51% | 4.95%
NR Type II | L=2 | Wideband 3bit | QPSK | 7.36% | 17.56%
 |  | Wideband 3bit + Subband 1bit | QPSK | 11.96% | 24.36%
 |  | Wideband 3bit | 8PSK | 12.00% | 21.21%
 |  | Wideband 3bit + Subband 1bit | 8PSK | 17.64% | 27.39%
Table 4. Type II vs Type I |  | 
 | Cell average gain | Cell edge gain
4T2R | ~18% | ~27%
32T2R | ~35% | ~49%

## Slide 11
UE complexity (8T2R, N1=N2=2, O1=O2=4, Rank1 feedback)
 | Type I | Type II
WB operation | Searching the best PMI within all the candidate PMIs by N1N2O1O2 candidate b， 4 candidate | Perform SVD decomposition with wideband H to obtain the most significant eigenvector V Searching the best L (2/3/4) DFT beams within all the beam groups and corresponding candidate DFT beams by V’b N1N2O1O2 candidate b The wideband amplitudes are the amplitude of V’b with the selected L beams
 | Complex multiplication in WB: ~5000 | Complex multiplication in WB: ~600
SB operation | Searching the best PMI within all the candidate PMIs by 1/4 candidate b， 4 candidate | Perform SVD decomposition with subband H to obtain the most significant eigenvector V The subband amplitudes and phases can be obtained by V’b with the selected L beams V’b N1N2O1O2 candidate b
 | Complex multiplication in SB: ~300 | Complex multiplication in SB: ~150
 | Type I | Type II
WB operation |  | Perform SVD decomposition with wideband H to obtain the most significant eigenvector V Searching the best L (2/3/4) DFT beams within all the beam groups and corresponding candidate DFT beams by V’b N1N2O1O2 candidate b The wideband amplitudes are the amplitude of V’b with the selected L beams
 | Complex multiplication in WB: ~5000 | Complex multiplication in WB: ~600
SB operation |  | Perform SVD decomposition with subband H to obtain the most significant eigenvector V The subband amplitudes and phases can be obtained by V’b with the selected L beams V’b N1N2O1O2 candidate b
 | Complex multiplication in SB: ~300 | Complex multiplication in SB: ~150
Taking 10 subbands as an example
  The total number of complex multiplication with Type I and Type II: 8120 and 2031
  Compared with Type I, the complexity at UE side for Type II is 25%
Note: complex multiplication is the most typical criterion to evaluate the UE complexity
Mandatory: Type 2 Codebook [2-41]

## Slide 12
At least a subset of type II NP codebook (as shown above) is mandatory.
[References] R1-1801809, UE capability of type II codebook, Huawei, HiSilicon, RAN#92
Type II NP- rank1/2 |  |  |  |  | 
Paremeters | port number | beam number | subband amplitude | subband phase | View
Value | 4 | L=2 | on/off | QPSK/8PSK | Mandatory
 | 8 | L=2 | on/off | QPSK/8PSK | Mandatory
 |  | L=3 | on/off | QPSK/8PSK | Mandatory
 |  | L=4 | on/off | QPSK/8PSK | Mandatory
Mandatory: Type 2 Codebook [2-41]

## Slide 13: Mandatory: SRS antenna switching [2-55]
  Support higher rank DL transmission
  With 4 Rx at UE side, support up to 4 layers DL transmission.
  In the TDD case, enable 4 antenna SRS switching (1T4T or 2T4T) for obtaining the full rank channel.
About 23% mean UPT gain can be observed over 2Tx switching for 2T4R/UE
About 26% mean UPT gain can be observed over 1Tx switching for 1T4R/UE

## Slide 14: UL/DL Ctrl, scheduling and HARQ

## Slide 15: PDCCH monitoring[3-5]
3-5: Minimum PDCCH monitoring occasion for a CORESET should be defined for different SCS[R1-1719401] , i.e,
  2OSs for 15kHz SCS
  4OSs for 30kHz SCS
  7 OSs for 60kHz SCS
  14 OSs for 120kHz SCS
Other possible PDCCH capabilities
  Number of BD for CA when the number of CC is greater than 4

## Slide 16: HARQ Processing Time [5-5][5-6]
[5-5][5-6] HARQ processing time for slot-based and non-slot based scheduling should be reported separately.

## Slide 17: Mandatory: GF Type 1 and repetitions [5-13/14, 5-19] (1/2)
GF type 1 (all transmission parameters configured by RRC without L1 signaling) is an effective tool to meet the NR latency requirements, for all use cases such as eMBB, URLLC and mMTC
GF type 1 is also beneficial to URLLC in terms of high reliability and resource utilization
GF type 1 is also beneficial and forward compatible for mMTC in terms of large energy saving and high resource utilization
K-repetition within a slot or between slot improves the system coverage and provides higher reliability

## Slide 18
Mandatory: GF Type 1 and repetitions [5-13/14, 5-19] (2/2)
Proposal: GF Type 1 is mandatory
Proposal: K repetitions within a slot should be mandatory for GF to ensure low latency with reasonable reliability
4 Repetitions
3 Repetitions
2 Repetitions
1 Repetition
Performance improvement by repetition combining
Latency reduction of GF-repetition over GB-Rx

## Slide 19: TDD operation in NR [3-6/5-1] (1/2)
Semi-static DL/UL assignment should be mandatory
  The DL/UL configuration is determined by cell-specific higher layer signaling and additionally UE-specific higher layer signaling if configured
    UE-specific higher layer signaling only overwrites the “unknown” state of the cell-specific higher layer configuration
  Support of cell-specific higher layer signalling should be mandatory without UE capability
  Support of UE-specific higher layer signalling should be mandatory with UE capability
  Reasons to be mandatory
    Most robust solution to avoid DL/UL interference among adjacent cells
    Compatible DL/UL configuration with LTE TDD UL/DL configuration(s)

## Slide 20: TDD operation in NR [3-6/5-1] (2/2)
Dynamic DL/UL assignment with dynamic SFI should be mandatory with UE capability (or optional)
  The DL/UL configuration is determined by cell-specific semi-static DL/UL assignment and dynamic SFI
    Dynamic SFI only overwrites the “unknown” state of the cell-specific semi-static DL/UL assignment
  Support of dynamic SFI monitoring should be mandatory with UE capability (or optional)
  Reasons to be mandatory with UE capability (or optional)
    Some benefits but not that significant
      More flexible DL/UL assignment compared to semi-static DL/UL assignment
      More robust to avoid DL/UL interference among adjacent cells compared to dynamic DL/UL assignment with DCI
    Need additional capability on dynamic SFI monitoring
Fully dynamic DL/UL assignment with DCI should be optional
  The DL/UL configuration is determined by DCI and/or configured periodic DL/UL signals
    No semi-static DL/UL configuration and no dynamic SFI
  Reasons to be optional
    May cause serious DL/UL interference among adjacent cells, especially of multiple operators
    More UE power consumption
      UE need to monitor PDCCH in every slot (even in UL-only slot) since UE doesn’t have any prior information on the slot format

## Slide 21: CA/DC, BWP, SUL

## Slide 22
Mandatory: Basic BWP operation [6-1]
6-1 Basic BWP operation
  1 UE-specific RRC configured DL BWP per carrier
  1 UE-specific RRC configured UL BWP per carrier
  RRC reconfiguration of any parameters related to BWP
  Note: UE-specific RRC configured DL/UL BWP can have the same or different numerology from the initial active DL/UL BWP
Proposal: Confirm 6-1 Basic BWP operation as mandatory without capability signaling

## Slide 23
Mandatory: BWP adaptation [6-2/3/4]
BWP adaptation
6-2 [Type A BWP adaptation with same numerology]: 2 configured BWP
6-3 [Type B] BWP adaptation with same numerology: 4 configured BWP
6-4 BWP adaptation with different numerologies
Proposal: The only difference between 6-2 and 6-3 is the number of configured BWP. RAN1 should avoid introducing such a small fragment feature. Remove 6-2 from the table.
Scenarios for BWP adaptation
    Scenario#1 : UE power saving ( 20-90% power saving depend on the ratio of wider BWP and narrow BWP)
        Adjust the RF bandwidth to reduce the energy consumption.
    Scenario#2: Dynamic resource sharing
        Enable resource sharing for different BWP with the same and different numerology. E.g. 1) eMBB UE can share the resource with URLLC BWP; 2) Low latency eMBB traffic can share its resource with large latency eMBB traffic
        Large system performance loss is observed (25-53% loss) due to lack of dynamic resource sharing if BWP switching with different numerology is an optional feature

## Slide 24
Mandatory: CA operation [6-5, 6-6]
DL NR-NR CA with same numerology [6-5]
Motivation: Basic DL NR-NR CA operation as mandatory if UE supporting CA band combination.
Merit: Data rate improvement
UL NR-NR CA with same numerology [6-6]
Motivation: Basic UL NR-NR CA operation as mandatory if UE supporting CA band combination.
Merit: Data rate improvement

## Slide 25
Mandatory: SUL and UL sharing [6-15/16/17/18/19]
7.5 kHz raster shift, mandatory without capability signaling for LTE re-farmed paired bands and SUL bands [6-15]
Already RAN1 agreement
Support LTE/NR UL in-band co-existence, NB-IoT inband operation in NR bands
RACH, PUSCH, PUCCH, SRS in a band combination including SUL, mandatory without capability signaling for UEs supporting SUL [6-16]
Basic SUL operation
Supplemental uplink with different numerology [6-17]
Should be merged into [6-16]
Likely deployment of 30kHz in NR band and 15kHz in SUL band, from the currently agreed SUL band combinations
Supplemental uplink with dynamic switch [6-18]
Should be merged into [6-16]
Significant throughput benefit to allow PUSCH transmitted (via TDM) on both NR and SUL carriers
Simultaneous Tx of SRS and PUSCH/PUCCH/SRS on SUL and non-SUL [6-19]
Optional with UE capability signaling
Not a “must” but requires additional RAN4 work

## Slide 26
Thank you !