## Slide 1: Narrowband measurement accuracy improvements
Feature lead Summary
3GPP TSG RAN WG1 Meeting #92 R1-1803033
Athens, Greece, February 26-March 2, 2018
Source: Ericsson
Title: Narrowband measurement accuracy improvements – Feature lead summary
Agenda Item: 6.2.6.3
Document for: Discussion and Decision

## Slide 2: RAN1#91 Status
WID RP-170852:
  Narrowband measurement accuracy improvements [RAN1, RAN4, RAN2]
    Evaluate and if appropriate specify use of additional existing signals than NRS for RRM measurements, with associated RAN4 core requirements taking into account e.g. UE complexity, power consumption, system capacity.
In RAN1#89, the following agreements were reached.
  For connected mode in the serving cell and idle mode in camped cell and neighbour cells, it is feasible from RAN1 point of view to use NSSS on an anchor carrier for RRM measurement
    RAN4 are requested to consider if NSSS is a suitable transmission
    How to use, i.e. if and/or under what circumstances to combine NRS with NSSS depend on RAN4 study
    Send an LS containing the above to RAN4, including the agreement from RAN1#88bis that “At least NSSS is used additionally to NRS for in-band, guard-band, standalone”
  Continue to study
    CRS for in-band operation mode
    NPBCH, NPDCCH, NPDSCH on an anchor carrier in the serving cell
In RAN1#91, an LS reply R1-1719333 from RAN4 to RAN1 states that
  RAN4 confirms that it is feasible to use NSSS on an anchor carrier for RRM measurement, under the working assumption that the ratio of NSSS EPRE to NRS EPRE is configured from {-3, 0, 3, spare} dB.
  RAN4 observes that the combination of NRS and NSSS can only provide limited gain compared to NSSS and will not consider this for RRM measurement.
  RAN4 identified that the antenna port(s) used for the measurement may vary arbitrarily across subframes and across cells in NSSS, and is still studying the potential impact of such variation. Solutions that might have RAN1 impact are not excluded from further study.

## Slide 3: RAN1#92 TDOC overview
In total 6 contributions were submitted to this agenda item:
TDOC | Title and Proposals | Source
R1-1801442 | Remaining details of NB-IoT measurements improvement Proposal 1: The combination of NRS with NSSS for RRM measurement accuracy improvement is not considered further in RAN1. Proposal 2: Only NSSS additionally to NRS is defined for RRM measurement enhancement during Release 15. | Huawei, HiSilicon
R1-1801496 | Narrowband measurement accuracy improvements for NB-IoT Proposal 1: Inform RAN4 that from RAN1 perspective, it is feasible to provide UE information of how to conduct the measurement when NSSS is configured to be used for RRM measurements, e.g., conveyed the information to the UE via RRC signaling. Proposal 2: When NSSS is configured and used for the NRSRP measurements in a cell intended for camping, the NRSSI measurement needed to calculate NRSRQ should not be made on subframes containing NSSS, NPSS, and NPBCH transmitted from the evaluate cell. Proposal 3: CRS is not a candidate for improving NB-IoT idle mode RRM measurements. Proposal 4: RAN1 should strive to limit the sum of the absolute power tolerance and the aggregated power control tolerance to ±9 dB. Proposal 5: RAN1 should consider connected mode anchor and non-anchor RRM measurements based on NPDCCH and NPBCH transmission. | Ericsson
R1-1801613 | Discussion on candidates for measurement improvement for NB-IoT Proposal 1: For in-band operation mode, CRS can be considered as additional signal for narrowband measurement. Proposal 2: NPBCH, NPDCCH and NPDSCH are not suitable for narrowband measurement improvement. Proposal 3: NSSS, CRS and cell specific WUS based measurement improvement shall be eNB configurable and optional. | ZTE, SaneChips
R1-1802173 | RRM measurement enhancement in NB-IoT Proposal: If CRS is used to enhance NRSRP measurement accuracy for in-band different PCI mode, CRS-based neighbour cell measurement enhancement should be supported together, at least UE should be able to generate CRS sequences and aware of power offset between NRS and CRS through assistant information | LG Electronics
R1-1802274 | Measurement accuracy improvement in NB-IoT Proposal 1: CRS can be used as additional signal for measurements. Proposal 2: Introduce signalling to support measurements using NRS and CRS for serving cell and neighboring cells. | Nokia, Nokia Shanghai Bell
R1-1802339 | Improvement of PHY measurements Proposal: Allow use of NPBCH and CRS in addition to NSSS which has already been agreed for serving cell and neighbour cell measurement purposes Cell specific/ common signalling may be introduced for each of these signals to indicate if it is okay to combine measurements from these signals with measurements from NRS. Additional signalling of TPR or combining weights may also be introduced to allow more flexible combining of the measurements. | Qualcomm Incorporated

## Slide 4: RAN1#92 TDOC Summary
Based on the contributions, the main open issues are identified as follows
  The use of LTE CRS in inband deployment mode addition to NSSS to improve the measurement accuracy for serving cell and neighboring cells
    Support: ZTE, SaneChips, LG Electronics, Nokia, Nokia Shanghai Bell, Qualcomm Incorporated
    Not support: Huawei, HiSilicon, Ericsson.
  The use of NPBCH, NPDSCH, NPDCCH in addition to NSSS to improve the measurement accuracy for serving cell and neighboring cells.
  When NSSS is configured for NRSRP measurements, how to provide UE information to conduct the measurement when NSSS is configured to be used for RRM measurements.
  If the definition of NRSSI in NRSRQ in TS36.214 should be updated for the scenario when NSSS is configured for NRSRP measurements.
  Whether connected mode improvements are targeted in Rel-14.
    If so, whether to limit the sum of the absolute power tolerance and the aggregated power control tolerance.
 | NPBCH | NPDSCH | NPDCCH
Support | Ericsson, Qualcomm Incorporated |  | Ericsson
Not support | Huawei, HiSilicon, ZTE, SaneChips, LG Electronics | Huawei, HiSilicon, ZTE, SaneChips, LG Electronics | Huawei, HiSilicon, ZTE, SaneChips, LG Electronics

## Slide 5: RAN1#92 Agreement, working assumptions, and conclusions made during offline discussions
  The combination of NRS with NSSS for RRM measurement accuracy improvement is not considered further in RAN1.
  NPDCCH, NPDSCH are not considered as a candidates in addition to NSSS, nor in combination with NSSS, to improve the measurement accuracy for serving cell and neighboring cells.
  Working assumption: It is feasible from RAN1 point of view to use NPBCH in addition to NRS for RRM measurement, to be confirmed by RAN4
    Ask RAN4 feedback on the combination of NPBCH with NRS
  FFS changes to the NRSSI definitions based on RAN1/4 agreements.

## Slide 6: RAN1#92 Continue discussion points after offline discussions
After the offline discussion, it is proposed to continue discussion within RAN1 that
  It is supported that UE can be configured to measure NSSS over 4 consecutive subframes
  When NSSS is configured for NRSRP measurements, how to provide UE information to conduct the measurement when NSSS is configured to be used for RRM measurements.
  WF
    R1-1803045 Way Forward on narrowband measurement accuracy enhancements

## Slide 7: RAN1#92 Proposed discussions
Due to potential RAN2 and RAN4 impacts, it is proposed RAN1 to discuss and try to conclude in this meeting
  Whether to use LTE CRS in inband deployment mode addition to NSSS to improve the measurement accuracy for serving cell and neighboring cells
  Whether connected mode improvements are still targeted in Rel-14.
    If so, which signal/channel should be used.
    If so, whether to limit the sum of the absolute power tolerance and the aggregated power control tolerance.
  If any agreements are made, inform RAN4 to study the feasibility and inform RAN2 the potential impacts on signaling design.