## Slide 1: WF on remaining issues for UL partial SF
Huawei, HiSilicon, …
3GPP TSG RAN1 #92
Athens, Greece, 26 February – 2 March 2018
Agenda Item: 6.2.2.1
R1-1803036

## Slide 2: Background
In RAN1 #91 meeting, the following agreements were achieved for UL partial SFs
If a UL grant schedules a UL burst by multiple-subframe scheduling operation with Mode 1, Mode 1 is applied for all subframes of the UL burst.
The TBS of the Mode 2 partial UL subframe is scaled by the factor of 0.5.
When UCI is sent along with UL-SCH, the UCI is rate-matched in the 2nd slot of a subframe with Mode 1 operation, regardless this Mode 1 subframe is actually full or partial.
UCI is rate-matched in the 2nd slot of the Mode 2 partial UL subframe.
The TBS of a subframe ending at symbol #6 is scaled by a factor of 0.5
UCI is rate-matched in the 1st slot of a subframe ending in symbol #6.

## Slide 3: Background
Still we have several issues that need to be further discussed as follows
The UCI mapping details for UL partial SF
  Calculation of Q’ for Mode 1/Mode 2/ending partial SF
  Mapping of RI for Mode 1, Mode 2, and ending partial
Additional UL ending positions

## Slide 4: Calculation of Q’
Amount of CSI physical resources Q’ is calculated as
For Mode 1 SF, the TBS of data, K, is not scaled. Therefore, Q’ of CSI should be calculated based on two slots regardless whether the actual transmitted SF is partial or full.
For Mode 2 and ending partial SF, K is scaled by 0.5. Therefore, Q’ of CSI should be calculated based on 1 slot.
Proposal 1: Amount of physical resources for UCI transmission is calculated based on two slots for Mode 1 SF and based on one slot for Mode 2 SF or ending partial SF.

## Slide 5: Mapping of RI
The mapping of RI on Mode 1, Mode 2 and ending partial SF can reuse the legacy mapping rule, i.e. besides the DMRS with 1 OS distance.
Proposal 2: RI is mapped on OS #1, #5 for ending partial SF, and mapped on OS #8, #12 for Mode 1 and Mode 2 SF.

## Slide 6: Additional ending positions
As we already introduced ending point at symbol 6, it is not necessary to further refine the TBS granularity of the ending partial subframe considering the increased overhead.
Proposal 3: No need to introduce additional ending points except symbol #6