## Slide 1: WF on transmit diversity
Ericsson, Huawei, HiSilicon, Nokia, NSB, NTT DCM, CATT
3GPP TSG RAN WG1 Meeting #92 R1-1803038
Athens, Greece, 26th March – 2nd March 2018
Agenda item – 6.2.3.3.1

## Slide 2: Background
From RAN1#90:
Working Assumption (may be revisited based on RAN4 response):
For designing PSSCH, RAN1 assumes the use of two-port non-transparent transmit diversity
  The use of non-transparent transmit diversity is configured.
  Details, including diversity scheme, are FFS
  Support of transmission and/or reception up to UE capability
    Note: It is RAN1 understanding that requirements on capabilities can be set at regional level and are outside 3GPP scope
  Send LS to RAN4 to ask their opinion about when non-transparent scheme for transmit diversity is used by Rel-15 UEs:
    Impact on Rel-14 UEs of PSSCH-RSRP measurement accuracy
    MPR for Rel-15 UEs
Non-transparent Transmit diversity is not used in the following cases:
  When communicating with Rel-14 UEs
  When there is a high probability of resource collision with Rel-14 UEs
Note: Some companies observe that the performance of MMSE-IRC receiver degrades when a non-transparent Transmit diversity scheme is used in interference limited scenarios with a dominant interferer

## Slide 3: Background
From RAN1#91:
Agreement
Assuming the previous WA of introducing non-transparent transmit diversity is confirmed, for two-port non-transparent transmit diversity for PSSCH, downselect option 1 as WA among the following candidate schemes
  Working assumption: Option 1: SFBC-based scheme (including PAPR preserving)
    FFS whether to apply slot-level PVS
  Option 2: STBC-based (including half symbol)

## Slide 4: Background
From R1-1801310, “LS reply on transmit diversity impact on V2X PC5,” RAN4:
A. Impact on PSSCH-RSRP measurement accuracy of Rel-14 UEs
Answer: RAN4 concluded that introduction of two-port non-transparent transmit diversity schemes in Rel-15 may lead to the impact on Rel-14 V2X UEs PSSCH-RSRP measurements accuracy. The impact depends on the two port DMRS design.
If Rel-15 two-port PSSCH DMRS does not include legacy Rel-14 DMRS sequence, Rel-14 UE will fail to perform PSSCH-RSRP measurements.
If Rel-15 two-port PSSCH DMRS includes legacy Rel-14 DMRS sequence, Rel-14 UE PSSCH-RSRP accuracy will degrade:
  For one type of PSSCH-RSRP measurement algorithm:
    -3 dB RSRP power offset will be observed comparing to the total RX power from the two DMRS APs.
    Almost no RSRP bias will be observed comparing to the RSRP from one antenna port.
    The variance of RSRP estimates may increase due to presence of interference from the second DMRS AP. Based on observation from some companies, the increase is limited.
  For a certain Rel-14 V2X UE implementation, it is observed that PSSCH-RSRP measurement is significantly impacted with certain DMRS designs. For some other DMRS design, the observed impact is the same as the first type of PSSCH-RSRP measurement algorithm.
  The impact on the resource selection and overall V2X performance is up to RAN1
  Note: RAN4 does not specify the PSSCH-RSRP estimation algorithm and it is left up to UE implementation.

## Slide 5: Background
From R1-1801310, “LS reply on transmit diversity impact on V2X PC5,” RAN4:
B. MPR for Rel-15 UEs
Answer: RAN4 concluded that among the three diversity schemes mentioned by RAN1, only SFBC may cause impact on the MPR. According to the simulation results, up to 0.5dB MPR increase is expected if SFBC is implemented.

## Slide 6: Background
From R1-1801310, “LS reply on transmit diversity impact on V2X PC5,” RAN4:
C. Impact on MMSE MRC receivers and advanced receivers in the a) presence of one interferer (single-port transmission and two-port diversity) b) presence of multiple interferers (single-port transmission and two-port diversity)
Answer: RAN4 made the following conclusions on the Rel-14 V2X UE demodulation performance in the interference limited environments in case of presence of two-port non-transparent transmit diversity interfering signals comparing to the single port interfering signals case:
For LMMSE-MRC receiver, the two-port non-transparent transmit diversity interfering transmissions have almost same impact as Rel-14 single-port interfering transmissions on receiving performance of Rel-14 UEs independent of single interferer or multiple interferers.
For LMMSE-IRC receiver, the performance impact depends on the propagation conditions and the following results were observed by companies:
  For low relative UE speed scenarios (~30km/h), the performance impact is as follows:
    For the case of single dominant interferer signal the performance loss is from 0.1 dB for low INR = 0 dB and is in the range from 3.2 to 4.5 dB for high INR up to 15 dB.
    For the case of two dominant interferer signals the performance loss is from 0 dB for low INR = 0 dB and is in the range from 1.0dB to 1.9 dB for high INR up to 15 dB.
  For high relative UE speed scenarios (~280km/h), the performance impact is generally less than 0.5 dB for all scenarios.
  The performance for LMMSE-IRC receiver is not worse than LMMSE-MRC receiver in the presence of two-port diversity interference.

## Slide 7: Proposal
Proposal:
Confirm the two working assumptions above