## Slide 1: WF on CW update for Autonomous UL in FeLAA
Broadcom, CableLabs, Charter, Comcast..
3GPP TSG RAN WG1 Meeting #92 R1- 1803041
Athens, Greece, 26th Feb – 2nd Mar 2018
Agenda item: 6.2.2.2.3

## Slide 2: Background (1)
In RAN1#91, the agreements made regarding Autonomous UL transmissions with Category 4 LBT included the following regarding the CW update mechanism:
  RAN1 shall specify the CWS adjustment for the case of no A/N reception until which the UE is not allowed to perform Cat.4 LBT and transmit AUL in case of no A/N or UL grant reception.
    FFS: Handling of ACK/NACK or UL grant in case multiple consecutive recent Cat.4 LBT AUL bursts were transmitted without waiting for any AUL-DFI or UL grant.
This WF provides proposals to address the above points

## Slide 3: Background (2)
Principle: Any Category 4 LBT that begins a new COT should use a contention window size that captures the result of the transmissions in the previous COT that started with Category 4 LBT.
This is also mandated by the ETSI BRAN harmonized standard EN 301 893 (section 4.2.7.2.3.6) in the following way:
  1) The Channel Access Engine shall set CW to CWmin. 2) The Channel Access Engine shall select a random number q from a uniform distribution over the range 0 to CW
  ……………
  7) When the Channel Occupancy Time (COT) has completed, and it has been confirmed that at least one transmission that started at the beginning of the Channel Occupancy Time was successful, the Initiating Device proceeds with step 1) above otherwise the Initiating Device proceeds with step 8) below. 8) The Initiating Device may retransmit. If the Initiating Device does not retransmit the Channel Access Engine shall discard all data packets associated with the unsuccessful Channel Occupancy Time and the Channel Access Engine shall proceed with step 1) above. Otherwise the Channel Access Engine shall adjust CW to ((CW + 1) × m ) – 1. If the adjusted value of CW is greater than CWmax the Channel Access Engine may set CW equal to CWmax. The Channel Access Engine shall proceed with step 2) above

## Slide 4: Background (3)
However, LAA requires at least 4 subframes between a Category 4 LBT transmission and the indication of its result through HARQ feedback
Given this, the following exception can be made for AUL transmissions that begin with Category 4 LBT
  Between two AUL transmissions that begin with Category 4 LBT , there shall be a Contention window update if there was sufficient time i.e. 4 subframes to receive the feedback corresponding to the former Category 4 LBT transmission.
In order to account for processing delay at the UE, a further margin of 1 or 2 subframes can be considered i.e. N = (4 + {1,2}) subframes. Please note that such a margin is not permitted by ETSI-BRAN and also risks being unfair to co-channel Wi-Fi which will update its contention window after every transmission in a COT that started with CAT4 LBT.
So, in our view, any value of N longer than 4+{1,2} cannot be justified in terms of a) the principle of fair channel access; b) the already existing agreement from RAN1#90 to make the AUL contention window update procedure to be the same as eLAA; and c) ETSI-BRAN harmonized standard.

## Slide 5: Background (4)
Further note that due to the delayed HARQ feedback in LAA and if N=6 is considered, there can be multiple transmissions that begin with Category 4 LBT 6 or more subframes earlier without any HARQ feedback in between.
Consider the following example:
  There are transmission bursts with Category 4 LBT at subframes n,n+2,n+4 and n+10. Transmissions in subframes n, n+2 and n+4 are in error.
  For LAA: HARQ feedback for transmissions in subframes n, n+2, n+4 is received in subframe n+12
  For Wi-Fi: Feedbacks are immediate
The next diagram shows the CW evolution for the following schemes:
  LAA alternative 1: N= 6, only 1 CW update irrespective of the number of Category 4 LBT transmissions that start 6 subframes or more earlier without a corresponding HARQ feedback
  LAA Alternative 2: N = 6, CW update for each outstanding Category 4 LBT transmission that start 6 subframes or more earlier without a corresponding HARQ feedback
  Wi-Fi
  Procedure specified in ETSI EN 301 893

## Slide 6: Background (5)
Observation:
CW update in Wi-Fi follows ETSI EN 301 893
CW update in Alternative 1 and Alternative 2
  Both do not follow ETSI EN 301 893.
  Both can be unfair to Wi-Fi since the CW used can be smaller that what is used in Wi-Fi.
  Alternative 2 is closer to what is specified in ETSI EN 301 893 since it leads to a CW update for each transmission burst that begins with Category 4 LBT.
  Alternative 2 is fairer to Wi-Fi

## Slide 7: Proposal
If a Category 4 LBT UL (SUL/AUL) transmission is initiated at least N subframes after the start of one or more previous Category 4 LBT UL(SUL/AUL) transmissions without the reception of any UL grant or AUL Downlink Feedback Information in between, where N = 6
  For each such previous Category 4 LBT (SUL/AUL) transmission initiated N or more subframes ago, after which no UL grant or AUL Downlink Feedback Information is received
    The contention window size of all priority classes at the UE is increased to the next higher value