## Slide 1: WF on UE to eNB COT sharing in Autonomous UL in FeLAA
Broadcom, CableLabs, Charter, Comcast,..
3GPP TSG RAN WG1 Meeting #92 R1- 1803043
Athens, Greece, 26th Feb – 2nd Mar 2018
Agenda item: 6.2.2.2.3

## Slide 2: Background (1)
The mechanism of a COT that is won by the eNB and then shared with UE(s) with a pause in between was allowed by ETSI-BRAN only to accommodate the grant-to-transmission delay in LAA, even though there is no equivalent procedure of sharing a COT with a pause in Wi-Fi.
Even when the shared/paused COT was allowed in LAA Release 14, it was ensured that the procedure is used only to overcome COT wastage that would otherwise happen due to the grant-to-transmission delay in LAA and not to provide aggressive channel access in other unrelated scenarios. For example, it was ensured that the eNB schedules contiguous UL transmissions within such a shared COT. The latter condition was put in order to not let the shared and paused COT be (mis)used for example to enable periodic UL VoIP transmissions with highest priority 25us LBT.
With the intention of expediting the transmission of AUL-DFI on the Downlink, we are willing to consider the extension of the shared COT mechanism such that a UE acquired COT can be shared with the eNB. This is even though there is no equivalent procedure in Wi-Fi and no protocol need for LAA to utilize this procedure, unlike for LAA Scheduled UL.

## Slide 3: Background (2)
However, in order to maintain fair coexistence with co-channel Wi-Fi, it has to be ensured that the eNB transmissions within a COT shared by the UE do not lead to channel access procedures that are more aggressive than corresponding Wi-Fi procedures. For example, the procedure must accommodate the following concerns:
  The ED threshold used in LBT depends on the maximum transmit power of the device. So, an eNB should not use a COT shared by the UE unless the maximum transmit power of the eNB is equal to or lower than the maximum transmit power of the UE. If this is not done, the UE will win the COT using a lower maximum transmit power and hence a higher ED threshold and then share it with an eNB that has a much higher maximum transmit power and hence would have normally used a lower ED threshold.
  This procedure, if allowed without restrictions, can be misused in multiple other ways. Consider the following example: An LAA eNB can have many UEs under its control. If such an eNB faces channel congestion around it causing it to increase its own Contention Window and wait longer, it can circumvent this procedure by making a UE that a) faces less congestion (the eNB is aware of the congestion observed by all its UEs and this information is communicated on the licensed channel); and b) potentially also has lower maximum transmit power, to win the channel with much higher probability and higher ED threshold and then hand over the COT to the eNB which it can use to transmit at a much higher maximum transmit power to all other UEs with only 25us LBT. Such a procedure will be very unfair to co-channel Wi-Fi.
  If the eNB is allowed to transmit many types of control messages within such a shared COT, it will let LAA gain an unfair channel access advantage over Wi-Fi which transmits all its control messages with CAT4 LBT with the exception of the Traffic Indication Map and Channel Switch Announcement which are typically transmitted < 1% of the time per AP. Equivalently, LAA already has DRS transmissions with 25us LBT that can be transmitted up to 5% of the time per eNB
  There is no grant-to-transmission delay if a UE shares its COT with an eNB. So, no pause can be allowed if the UE shares it COT with the eNB.

## Slide 4: Proposal
A UE initiated COT using Cat4 LBT can be shared with the eNB to allow PDCCH only transmission carrying DL control information.
The eNB can utilize the COT acquired by the AUL UE to transmit DL control information only if it starts transmission within 25 us from the end of the AUL burst.
eNB does not need to perform LBT within a UE acquired COT if the gap is <= 16 us.
eNB uses Type 2 channel access (25 us LBT) within a UE acquired COT if the gap <= 25 us.
For PDCCH transmission within a UE acquired COT, the PDCCH transmission is limited to a partial ending subframe of up to 3 OS length.
The eNB shall send AUL DFI to the UE which acquired the COT within the indicated DL subframe.
The eNB may send control information (AUL-DFI or PDCCH) to any UE provided that the transmission duration does not exceed the minimum time required to transmit AUL DFI and PDCCH control information to the UE which acquired the TXOP.
The transmit power of the eNB for transmissions within the shared COT shall not exceed the transmit power used by the UE to derive the ED threshold for CAT4 LBT that acquired the COT.
UL-DL-UL sharing is not allowed.
The remaining MCOT and LBT priority class is indicated to the eNB through the AUL-UCI.